GPS exercise (group A)

- Make teams (mix of experienced with inexperienced)

- Explore the GPS and familiarize yourself.

- Configure the GPS UNITS to “wgs84” and “UTM” and “metric units” in the set-up menu

- Find a clear spot outside where you can get a good reception

- Acquire signal (can take 5 to 10 minutes)

- Enter waypoints

  - In the satellite view: press down “Enter” until –MARK WAYPOINT appears and press “Enter” for “OK”

  - Repeat 5x to create 6 waypoints)

  - Select MENU- WAYPOINTS

  - Select WAYPOINT 001

  - Select COORDINATES (arrow down) – PRESS ENTER

  - Change figures according to the table below

  - Repeat c,d,e for waypoints 002 – 006

  - Show your set-up to the facilitator

- Go to the starting point indicated by your facilitator

- Again SELECT WAYPOINT 001 and press GOTO

- Navigate to waypoint 001 (what is the distance?)

- At waypoint 001 select 002 and navigate there.

- repeat until you reach 006

- The exercise is now finished

| 001 | 002 | 003 | 004 | 005 | 006 |
| --- | --- | --- | --- | --- | --- |

GPS exercise (group B)

- Make teams (mix of experienced with inexperienced)

- Explore the GPS and familiarize yourself.

- Configure the GPS UNITS to “wgs84” and “UTM” and “metric units” in the set-up menu

- Find a clear spot outside where you can get a good reception

- Acquire signal (can take 5 to 10 minutes)

- Enter waypoints

  - In the satellite view: press down “Enter” until –MARK WAYPOINT appears and press “Enter” for “OK”

  - Repeat 5x to create 6 waypoints)

  - Select MENU- WAYPOINTS

  - Select WAYPOINT 001

  - Select COORDINATES (arrow down) – PRESS ENTER

  - Change figures according to the table below

  - Repeat c,d,e for waypoints 002 – 006

  - Show your set-up to the facilitator

- Go to the starting point indicated by your facilitator

- Again SELECT WAYPOINT 001 and press GOTO

- Navigate to waypoint 001 (what is the distance?)

- At waypoint 001 select 002 and navigate there.

- Repeat until you reach 006

- The exercise is now finished

| 001 | 002 | 003 | 004 | 005 | 006 |
| --- | --- | --- | --- | --- | --- |