## Slide 1
Drought Monitoring and Assessment
Professor Bob Su ITC, University of Twente, The Netherlands
z.su@utwente.nl

## Slide 2: What is the difference?

## Slide 3: 1. Comprehend basic ideas for estimating water availability 2. Be able to identify methods & data products for deriving different water availability terms 3. Familiarize with the applications in drought monitoring and assessment
Learning Objectives

## Slide 4
(O. Heffernan)

## Slide 5
(O. Heffernan)

## Slide 6
(O. Heffernan)

## Slide 7: What Is Drought and How To Detect It?
Drought may be defined as the lack of water of a certain location in a certain period compared to a climatic average.
From a climatic perspective, we may distinguish meteorological, soil moisture and hydrological drought.

## Slide 8: What Is Drought And How To Detect It?
Meteorological drought refers to a shortage of precipitation compared to a climatic average.
Soil moisture drought can be caused by a shortage of precipitation, excessive evaporation and transpiration due to dry weathers and lack of irrigation.
Hydrological drought is caused by a combination of lack of precipitation and excessive use of available water resources.
When the impact of drought is also taken into consideration, four types of droughts are usually defined such as meteorological drought, agricultural drought, hydrological drought and socioeconomic drought.

## Slide 9: Remote Sensing Provides Real-time Spatial Observations
Q&A:
How shall we detect & predict drought?
Assessment and monitoring of drought characteristics:
its intensity, duration and spatial extent in terms of:
  atmospheric and land surface variables - precipitation, evapotranspiration, soil moisture and vegetation conditions
Prediction of drought:
  Spatial observations coupled to modelling and forecasting of the water cycle -> information on future drought for drought preparedness

## Slide 10
Let there be light
(NASA)

## Slide 11
Water cycle and its link to climate
(Su et al., 2010, Treatise on Water Science)

## Slide 12
Wind
Solar Radiation
Land-Atmosphere Interactions
- Terrestrial Water, Energy and Carbon Cycles
Sensible Heat
(diffusion/convection)
Gases
Soil Heat
(Conduction)
Thermal radiation
Latent Heat
(Phase change)
Precipitation
Biochemical
Processes
Water &
Vapour
Advection

## Slide 13: Drought Indices (Lots Of Them)
Percent of Normal (PN)
Standard Precipitation Index (SPI)
Palmer Drought Severity Index (PDSI)
Crop Moisture Index (CMI)
Surface Water Supply Index (SWSI)
Reclamation Drought Index (RDI)
Evapotranspiration Deficit Index (ETDI)
Eden, U. (2012) Drought assessment by evapotranspiration mapping in Twente, the Netherlands. Enschede, University of Twente, Faculty of Geo-Information and Earth Observation (ITC), 2012.

## Slide 14
Wet Condition: Maximum Transpiration
Transpiration limited by plant water availability in the root zone
What is Drought ?
Dry Condition: No transpiration

## Slide 15: Quantitative Approaches for Drought Monitoring and Prediction
Approach 1: Surface Energy Balance
  To derive relative evaporation & relative soil moisture in the root zone from land surface energy balance
  To define a quantitative drought severity index (DSI) for large scale drought monitoring
Approach 2: Soil Moisture Retrieval
  To determine surface soil moisture
  To assimilate surface SM into a hydrological model to derive root zone soil moisture
Approach 3: Total water budget

## Slide 16
Climate & Satellite Information System
Drought Monitoring & Prediction
Decision Makers
Meteorological Data
Surface Energy Balance System (SEBS)
Internet
Surface Soil Moisture
Data Assimilation
(to infer root zone water availability)
Drought Information System (Drought Severity Distribution)

## Slide 17: From Energy Balance to Water Balance
R: Relative Plant Available Soil Water Content
DSI: Drought Severity Index
(Su et al., 2003, PCE)

## Slide 18: Relationship between evaporative fraction to surface variables (albedo, fractional vegetation coverage and surface temperature) -> root zone soil moisture
The relative evaporation is given as

## Slide 19: Relationship of evaporative fraction to surface variables (albedo, fractional vegetation coverage and surface temperature)
The relative evaporation is given as
The SEBS algorithm (Su, 2002, HESS)

## Slide 20: Relationship of evaporative fraction to surface variables (albedo, fractional vegetation coverage and surface temperature)

## Slide 21: Relation of evaporative fraction to surface variables (an example)

## Slide 22: Normalized temperature difference versus albedo

## Slide 23: Normalized temperature difference versus albedo
Q&A:
What else shall we do?
What other information can we use?

## Slide 24: Normalized temperature difference versus albedo

## Slide 25
Comparison to Soil Moisture Measurements
Relative evaporation vs relative soil moisture
Time Series of Drought Severity Index

## Slide 26: Tibetan Plateau observatory of plateau scale soil moisture and soil temperature (Tibet-Obs)
Su et al. 2011, Hydrol. Earth Syst. Sci.
www.hydrol-earth-syst-sci.net/15/2303/2011/
ESA Dragon programme
EU FP7 CEOP-AEGIS
EU CORE-CLIMAX
NWO-GO SMAP F/T

## Slide 27: Preliminary validation results
Mean sm at Maqu site (depth of 5 cm)
VUA-NASA sm from AMSR-E data
Organic soils
Sandy loam soil

## Slide 28
Quantification of uncertainties in global products
(Su et al., 2011, HESS)

## Slide 29: Maqu SMST Network – validation results

## Slide 30: Ngari SMST Network – validation results

## Slide 31: How can we use this information for drought monitoring and prediction?
Q/A: any other way to combine information?

## Slide 32
WACMOS.org

## Slide 33: Water Budget Closure
Land Surface & Water Use
River discharge
Groundwater
Rain
Snow
evaporation
Surface Water

## Slide 34
Q/A: how to put up a real time system?
How do we decide if there is a drought?

## Slide 35: Water Budget Closure
Land Surface & Water Use
River discharge
Groundwater
Rain
Snow
evaporation
Surface Water
SPI
SPEI,
SDSI-ETDI,
STWSI
SVCI

## Slide 36: Standardized Indices
SPI: Standardized Precipitation Index,
SPEI: Standardized Precipitation Evaporation Index,
SDSI-ETDI: the Standardized Drought Severity Index-Evapotranspiration Deficit Index,
SVCI: Standardized Vegetation Condition Index,
STWSI: the Standardized Terrestrial Water Storage Index
  all calculated on weekly or monthly time interval from 1 to N time intervals (e.g. for 48 months) (i.e. as anomalies and cumulative anomalies)

## Slide 37: How shall we define droughts?
Dark blue is less than one standard deviation from the mean. For the normal distribution, this accounts for 68.27% of the set; while two standard deviations from the mean (medium and dark blue) account for 95.45%; and three standard deviations (light, medium, and dark blue) account for 99.73%. (wikipedia)

## Slide 38: How shall we define droughts?
The probability that a normal deviate lies in the range μ − nσ and μ + nσ is,
Value range | category
μ−1σ < F > μ+1σ | Near normal
μ−2σ < F <= μ-1σ | Moderately dry
μ−3σ < F <= μ-2σ | Severely dry
F <= μ-3σ | Extremely dry
μ+1σ <= F < μ+2σ | Moderately wet
μ+2σ <= F < μ+3σ | Severely wet
μ+3σ <= F | Extremely wet

## Slide 39
GLDAS derived Standardized total water storage index – drought situation

## Slide 40: What is consistency among different physically interrelated variables (Spatial Water budget of the Yangtze River Basin)
dS/dt

## Slide 41: Yangtze River Basin
Upper Yangtze reach, from Tuotuohe, to Yichang.
Middle reach from Yichang to Hukou.
Lower reach extends from Hukou to the river mouth near Shanghai.
Cuntan, Yichang, Hankou, and Datong are four gauging stations located along the mainstream of the Yangtze.

## Slide 42
Closure of Water Cycle over a river basin
Total water Storage(TWS)
In-situ & satellite Observations
Reanalysis
Satellite Observations
Notes: For water balance issue, this equation is usually used.
The left hand side of the equation represents the change of total water storage, the right hand side says that the total water storage change equals to precipitation minus evaporation and minus runoff.
In this calculation, the precipitation is from GPCP, the evaporation is calculated by SEBS, the runoff is from in-situ observation. This results represent the consistency validation among in-situ observation datasets.
Except for in-situ observation datasets, ERA-Interim has these three variables as well, so era-interim results will be applied with this equation to calculate the total water storage change as well, from reanalysis point of view.
On the other hand, the total water storage can be measured by using GRACE, which is from remote sensing point of view.
So, by this approach, we can assess if different source of data are consistent to each other or not.

## Slide 43: Seasonal average maps of sensible heat flux (H) (a) Mar-May, (b) Jun-Aug,(c) Sep-Nov, (d) Dec-Feb

## Slide 44
TWS Anomaly (Yichang)
Notes: Ok, then, this is the result for Yichang station. From here, we can see that the total water storage anomaly derived from the observation data and from ERA reanalysis data are consistent with each other, indicating both datasets capture the surface dynamics of the water cycle fluxes.
However, the GRACE derived anomaly has somehow larger amplitudes than the other two, which may be indicating deep groundwater contribution.

## Slide 45: Cumulative TWS anomaly at Upper Reach (Yichang station)
GRACE data
(ver: RL05.DSTvSCS1401)
(ver: RL04 ssv201008)

## Slide 46: MSc Thesis Drought Monitoring And Assessment Using Remote Sensing By: Peter Muiruri
WREM 2017/18

## Slide 47: The Standardized Indices framework
SPI (McKee et al., 1993)
    Precipitation (P) is the only input, (+30yrs rainfall ideal)
    Multiscalar: staggered from 1-48months scale
    Precipitation record normalized using the Gamma PDF before transformation to a Gaussian multivariate
SPAEI (Homdee et al., 2016); substituted SPEI (Vincente-Serrano et al., 2010)
    Combines P and ETa; >Multiscalar
    Normalized using the GEV PDF
SVI (Peters, 2002)
    NDVI values are standardized :
STWSI
    TWS standardized similarly as the SVI >Multiscalar
Sustained negative values show drought.

## Slide 48: Study area- Yangtze river basin, china
River Yangtze sourced in the Qinghai-Tibetan Plateau.
Flows 6300km eastwards to the sea.
Cuntan forms the entrance to the 600km long Three Gorges Dam

## Slide 49: data

## Slide 50: Methodology
  Calculate the SDI and estimate WB agreement

## Slide 51: Cont.… Cuntan area Time series
SPI/SPAEI
Notes: The SPI appears to overestimate the wet periods and underestimate some of the severe
drought events. Two instances where this happens is between in 2006 summer drought and in the 2009/10
winter drought.

## Slide 52: Results Basin mean Time series
Notes: At longer lengths, SVI has 3-phase evolution, slowly to changes in P and ET.

## Slide 53: Temporal drought Evolution in 2006 & 2010
Jan 2006
July 2006
Notes: 2003: Mostly wet in the upper zones. Drought well defined at SPI-6, 9 and 12.
2010: Largely a dry year. Most of the mainland and areas in the upper zones dry. Most rainfall in the year is around areas close to sea (South west corner), suggesting convective rainfall.

## Slide 54: Temporal drought Evolution in 2006 & 2010
Jan 2010
July 2010
Notes: 2003: Mostly wet in the upper zones. Drought well defined at SPI-6, 9 and 12.
2010: Largely a dry year. Most of the mainland and areas in the upper zones dry. Most rainfall in the year is around areas close to sea (South west corner), suggesting convective rainfall.

## Slide 55: Cont.… WATER Balance
Good agreement and consistency:- adequate capture of surface water fluxes dynamics
Peaks spikier in R(obs) than in R(calc) due to dam water-release in June
In winter, TWS decreases as water leaves the catchment (water release as groundwater or as surface runoff) and R increases, P replenishes TWS flux outflow in summer.
Distinct pattern in WB deficits appearing to occur/coincide with reported drought event
Notes: TWS gradually increases through the monsoon and is maximum in August as P replenishes the released winter flux. Discharge is concentrated in one period, possibly when the reservoir is being filled.

## Slide 56: Conclusion
The proposed SDI framework is feasible
SPAEI show higher severity and longer drought durations compared to SPI, probably because the SPAEI incorporates ETa.
SPI and SPAEI infer changes occurring at shallow depth and on surface, good for meteorological drought. STWSI infer deep-water horizons and TWS. STWSI and SPAEI can compliment each other in monitoring hydrological drought. SVI is limited as is affected by phenology and influenced by meteorological forcing
R(calc) overestimates runoff in winter through summer except for June where the observed runoff is twice the calculated runoff due to the dam-water release
No WB closure. PBIAS in accumulated annual averages is small (8.85%). Distinct pattern in WB deficits appearing to occur/coincide with reported drought event
Notes: SPI record is climatic and more representative and SDI are consistent
SPAEI was found to have higher severity and longer drought durations compared to SPI, probably because the SPAEI incorporates ETa.
SPI and SPAEI -infer changes occurring at shallow depth and on surface, good for meteorological drought
STWSI infer deep-water changes, and SM changes at depth. SPAEI incorporates ETa, SPAEI and STWSI is recommended.

## Slide 57: Water Budget Closure
Land Surface & Water Use
River Discharge
Groundwater
Rain
Snow
evaporation
Surface Water
SPI
SPAEI
STWSI
SVCI

## Slide 58: Impacts and projections in water resources
Q1: What are observed impacts to water resources in Yangtze due to climate and human changes ?
Q2: Will the changes in the Yangtze River Basin influence the East Asian monsoon patterns?
Q3: What will be the spatial/temporal distribution of water (sediment) resources in 21st century ?
Water resource shift?

## Slide 59: Referances/Further Readings
Chen, X. Z.Su et al, 2014, Development of a 10-year (2001–2010) 0.1-degree dataset of land-surface energy balance for mainland China, ACP, 14 (2014)23, pp. 13,097-13,117.
Su, Z., 2002, The Surface Energy Balance System (SEBS) for estimation of turbulent heat fluxes, Hydrol. Earth Syst. Sci.,, 6(1), 85-99.
Su, Z., A. Yacob, Y. He, H. Boogaard, J. Wen, B. Gao, G. Roerink, and K. van Diepen, 2003, Assessing Relative soil moisture with remote sensing data: theory and experimental validation, Physics and Chemistry of the Earth, 28(1-3), 89-101.
Su, Z., Fernández-Prieto, D., Timmermans, J., Xuelong Chen, Hungershoefer, K., Roebeling, R., Schröder, M., Schulz, J., Stammes, P., Wang, P. and Wolters, E. (2014) First results of the earth observation Water Cycle Multi - mission Observation Strategy (WACMOS). Int. J. Appl. Earth Obs. Geoinfor., 26 (2014) pp. 270-285.
Su, Z., Y. He, X. Dong, L. Wang, 2017, Chapter 8, Drought Monitoring and Assessment Using Remote Sensing, V. Lakshmi (ed.), Remote Sensing of Hydrological Extremes, Springer Remote Sensing/Photogrammetry, DOI 10.1007/978-3-319-43744-6_8

## Slide 60: Yes, it is water availability!
Final Q/A,
How important is all this fuss?

## Slide 61: How acute is it to deal with drought ?
Too little water: In my city of Cape Town, there is only one topic of conversation: water http://www.cnn.com/2018/02/01/opinions/cape-town-water-crisis-opinion-joseph/index.html

## Slide 63
Thank you very much for your attention!