## Slide 1
Pre-processing and multi-temporal analysis of SAR time series
Magdalena Fitrzyk

## Slide 2
Part 1
Multitemporal Analysis of SAR Backscatter Intensity

## Slide 3: Objectives
Familiarizing with SNAP toolbox
Familiarizing with Sentinel-1 GRD prodcucts
Calculation of backscatter intensity from Sentinel-1 detcted products
Analysis of temporal backscatter signatures for various land cover types
Change detection over AOI (Beijing Daxing International Airport)

## Slide 4: Introduction
S1A_IW_GRDH_1SDV_20151003T222044_20151003T222111_007994_00B2F6_9374 S1A_IW_GRDH_1SDV_20160611T222046_20160611T222112_011669_011DDC_7FB0 S1B_IW_GRDH_1SDV_20171115T222014_20171115T222041_008298_00EAE8_2415 S1B_IW_GRDH_1SDV_20181110T222021_20181110T222048_013548_019131_A556 S1B_IW_GRDH_1SDV_20190930T222028_20190930T222054_018273_022698_C498
Input data: time series of Sentinel-1 GRDH images over China
Output:
temporal backscatter signatures for various land cover types
change detection

## Slide 5: Data preparation
1. Opening the S1 data
For unzipped products

## Slide 6: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 7: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 8: Updating orbits
Radar / Apply orbit file
POEORB - few weeks after acq.
The orbit file provides accurate satellite position and velocity information. Based on this information, the orbit state vectors in the abstract metadata of the product are updated.
RESORB – within few hours

## Slide 9: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 10: Radiometric Calibration
Beta Naught – radar brightness coefficient, reflectivity per unit area in slant range which is dimensionless
Sigma Naught – power returned to the antenna from the ground (distributed scatterer) in dB. A number comparing the strangth of the signal to that expected from and area of one square meter. It is defined with respect to the nominal horisontal plane and is varying with incidence angle, wavelength, polarisation and scattering surface itself
From image pixel values or digital numbers (DNs) we can derive:

## Slide 11: Radiometric Calibration
Pixel values can be directly related to the radar backscatter
Radar/Radiometric/Calibrate

## Slide 12: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 13: Terrain correction & Geocoding
Point B with elevation h above the ellipsoid is imaged at position B’ in SAR image, though its real position is B". The offset between B' and B" exhibits the effect of topographic distortions
Terrain Correction allows geometric overlays of data from different sensors and/or geometries.

## Slide 14: Terrain correction & Geocoding
Radar / Geometric / Terrain Correction / Range Doppler Terrain Correction

## Slide 15: Terrain correction & Geocoding
DEM selection
Pixel spacing
Map projection
Masking areas without elevation

## Slide 16: Data check

## Slide 17: Automatic Processing with Graph
Graph Builder
Inserting blocks with particular processing operators
(right mouse button)
Save the graph and/or Run

## Slide 18: Automatic Processing with Graph – Calibration, Terrain Correction
save as GRD_Cal_TC.xml
The same settings like in manual processing
Apply Orbits: Sentinel Precise
Calibration: Output Sigma0
Terrain Correction: pixel spacing 10m

## Slide 19: Batch processing
Adding data products
Batch processing tool
Loading the graph

## Slide 20: Batch processing
Open previously saved graph GRD_Cal_TC.xml

## Slide 21: Time series analysis
Add your data products

## Slide 22: Time series analysis
Bands filter
Show plot at cursor position
Choose your processed data products

## Slide 23: Time series analysis
One of the plottet bands has to be opened

## Slide 24: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 25: Creating multitemporal stack
Product geolocation (if terrain corrected)
Orbits (if not terrain corrected)
Collocating spatially overlapping images

## Slide 26: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 27: Multitemporal speckle filtering
Spatial filtering with weighted average of selected filter across the images of the time series

## Slide 28: Multitemporal speckle filtering
Not filtered
Filtered

## Slide 29: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 30: Conversion from linear to dB

## Slide 31: Conversion from linear to dB

## Slide 32: Linear vs dB comparison

## Slide 33: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 34: Visual inspection of the time series

## Slide 35: RGB Composite
Right click on the product
Band selection

## Slide 36: RGB Composite
Red – high backscatter in 2015, low backscatter in 2019
Cyan – low backscatter in 2015, high in 2019

## Slide 37: Stack averaging

## Slide 38: Stack averaging – RGB Composite
RGB combination for land cover classification

## Slide 39: Image statistics
Choose your band

## Slide 40: Image statistics - polygon
Draw the polygon

## Slide 41
Part 1
Multitemporal Analysis using SAR Coherence-Intensity composites

## Slide 42: Objectives
Familiarizing with Sentinel-1 SLC prodcucts
Calculation of backscatter intensity from Sentinel-1 SLC products
Calculation of interferometric coherence
Analysis of coherence and intensity false colour composites

## Slide 43: Introduction
S1A_IW_SLC__1SDV_20151003T222043_20151003T222111_007994_00B2F6_4C0E.zip
S1A_IW_SLC__1SDV_20171115T222013_20171115T222041_008298_00EAE8_F7A2.zip
Input data: set of two Sentinel-1 SLCs
Output: coherence – intensity false colour composites for land cover mapping and change detection

## Slide 44: Sentinel-1 data acquisition
Terrain Observation
by Progressive Scans
(TOPS)

## Slide 45: Sentinel-1 TOPS Data Handling and Processing
Bursted IW SLC
TOPSAR Split to choose a subswath and bursts for the AOI

## Slide 46: Sentinel-1 TOPSAR Split
Radar/Sentinel-1 TOPS/S-1 TOPS Split
Selection of subswath
Selection of polarization
Selection of bursts
TOPS Split applied to both S-1 SLCs
IW1
VV
2-5

## Slide 47
STEP 1
Interferometric Coherence

## Slide 48: Coregistration
S1A_IW_SLC__1SDV_20151003T222043…
S1A_IW_SLC__1SDV_20171115T222013
Coregistered bands in one product
Co-registration of two S-1 SLC split products (master and slave) of the same sub-swath using the orbits of the two products and a Digital Elevation Model (DEM).
ESD estimates the range and azmiuth offset (exploiting the data at the overlapped area of the adjacent bursts) and performs range and azimuth corrections for every burst in the slave image

## Slide 49: Interferometric Coherence
COHERENCE
Measure of correlation between phase in two SAR complex images
Ranging from 0 (no correlation) to 1
Coherence may be affected by:
Local slope
Properties of the surface
Time lag between acquisitions
The perpendicular baseline
Poor coregistration

## Slide 50: Interferometric Coherence
Demarcation black-filled line between bursts
Radar/Interferometric/Products/Coherence

## Slide 51: S-1 TOPS Debursting
Radar/Sentinel-1 TOPS/S-1 TOPS Deburst
Input: Coherence

## Slide 52: Terrain Correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
+ Geocoding
Select:
DEM
Resampling
Pixel spacing
Projection
Pixel spacing 20m

## Slide 53
STEP 2
Backscatter Intensity

## Slide 54: Backscatter Intensity product
Input: Two splitted SLCs
MENU: Graph Builder + Batch processing tool

## Slide 55: Creating a stack
Input: Coherence from STEP 1
Intensity backscatter for 2 SLCs from STEP 2

## Slide 56: Conversion of sigma0 to db
Right click on the sigma0 band
Conversion linear to/from db
Right click on the sigma0_db virtual band
Select „convert band”
Save the product: File/Save product

## Slide 57: Band math: average sigma 0 and difference
Sigma0 difference
Sigma0 average

## Slide 58: Creating RGB false composite
Right click on the stack product
Open RGB Image Window
Select RGB bands:
R: coherence
G: average sigma0
B: difference sigma0

## Slide 59: Resulting RGB false composite
Multi-temporal product (2015-2017)
Yellow: Urban centers
Magenta: objects not changing
Green: Vegetated lands and forests
Blue: objects that changed

## Slide 60
2015
2017

## Slide 61
2015
2017