## Slide 1
Introduction to ESA toolboxes
Magdalena Fitrzyk

## Slide 2: SNAP
Free and open source software
Common Java core framework
Joint development of SNAP platform for Sentinel and other toolboxes
Interchangeable Java/Python plugins
Portable engine to Cloud infrastructure
User friendly: single installation, intuitive GUI, online help, tutorials, active user forum
SNAP
SeNtinel Application Platform
Sentinel-1 Toolbox
Sentinel-2 Toolbox
Sentinel-3 Toolbox
SMOS Toolbox
PROBA-V Toolbox
Download it at
step.esa.int

## Slide 3: SNAP downloads & STEP visits
SNAP download exceeded 425.000 from June 2015 until today
STEP website exceeded 775.000 visit sessions from June 2015 until today

## Slide 4: SNAP & SAR (Sentinel-1 Toolbox)
  Main features: Absolute calibration, Multilooking, Speckle filtering, Precise orbits handling
  Coregistration of detected and complex products
  Full support of Sentinel-1 TOPS interferometry, debursting, slice assembly
  Terrain Correction
  SAR simulation and Layover and shadow masks
  Applications: oil spill detection, ship detection, wind field estimation etc.
  Fully integrated and featured InSAR tools for Stripmap and Zero-Doppler focused data
  Compatibility with PolSARpro Toolbox (Reader, Writer)
  Integrated Export to SNAPHU (interferometric phase unwrapping) and STAMPS (PS InSAR)
Sentinel-1
ENVISAT
ERS-1
TerraSAR-X
ALOS 1&2
KOMPSAT-5
RADARSAT
ICEYE
COSMO-SkyMed

## Slide 5: Sentinel-1 characteristics
Main features:
C-band (5.4 GHz) SAR
Daily coverage of high priority areas
Bi-weekly global coverage
12 days repeat cycle (6 days with both Sentinels 1A and 1B operational)
7 years design life time (consumables for 12 years)
Applications:
Ice and marine/land monitoring
Mapping in support of humanitarian aid in crisis situations

## Slide 6: Sentinel-1 characteristics

## Slide 7: Sentinel-1A & B data
Available products
Level 0 (L0-RAW)
Level 1 Ground Range, Multi-Look, Detected Medium Resolution (L1-GRDM) and High Resolution (L1-GRDH)
Level 1 Single-Look Complex (L1-SLC)
Level 2 Ocean (L2-OCN)
S-1 A/B
S-1 A/B
S-1 A/B
S-1 A/B
2018
1,304,078 published products
(2.3 PB)
3,282,679 published products
from start of Ops to the end Y2018 (~5.8 PB)

## Slide 8: SNAP & Optical HR (Sentinel-2 Toolbox)
  Main features:
  Sen2Cor and i-Cor for Atmospheric Correction
  L2B biophysical processor (LAI, fAPAR, …)
  Reflectance to Radiance Processor
  Radiometric Indices
  Vegetation indices: DVI, RVI, PVI, IPVI, WDVI, TNDVI, GNDVI, GEMI, ARVI, NDI45, MTCI, MCARI, REIP, S2REP, IRECI, PSSRa
  Soil indices: SAVI, TSAVI, MSAVI, MSAVI2, BI, BI2, RI, CI
  Water indices: NDWI, NDWI2, MNDWI, NDPI, NDTI
  IdePix Processor: pixel classification
  OTB tools: Pansharpening, Rasterization, Segmentation, …
Sentinel-2
SPOT
Pleiades
Landsat
ALOS AVNIR
RapidEye
Kompsat
Ikonos
Worldview
……

## Slide 9: Sentinel-2 characteristics
Optical mission for the monitoring of land and coastal regions
Main features:
Constellation of two satellites (Sentinel-2A and Sentinel-2B)
Multi-Spectral Instrument (MSI)
Polar, sun-synchronous orbit at 786km and LTDN 10h30
10 days repeat cycle (5 days with both Sentinels 2A and 2B operational)
Swath of 290km

## Slide 10: Sentinel-2 products
SENTINEL-2 products available for users (either generated by the ground segment or by the SNAP) are:
Level-1C
Top-Of-Atmosphere reflectances in cartographic geometry
Systematic generation and online distribution
~600MB (each 100km x 100km)
Level-2A
Bottom-Of-Atmosphere reflectances in cartographic geometry
Systematic and on-User side (using SNAP)
~600MB (each 100km x 100km)
Products are a compilation of elementary granules of fixed size, along with a single orbit. A granule is the minimum indivisible partition of a product (containing all possible spectral bands).
For Level-1C and Level-2A, the granules, also called tiles, are 100x100 km2 ortho-images in UTM/WGS84 projection.

## Slide 11: Sentinel-2 applications
Band 11
B11
Regional to Urban Applications
Geology
Emergency management
Global Land use
& change
Coastal zones/bathymetry
Glaciers & Ice
Land cover classification, high resolution layers & change
Agriculture, Forests & Carbon, Vegetation monitoring
Water quality

## Slide 12: SNAP & Optical/Thermal MR (S3 Toolbox)
Sentinel-3
ENVISAT
Proba-V
SPOT VGT
MODIS
AVHRR
VIIRS
ERS
……
  Main features:
  Visualizing spectrum of pixels
  Uncertainty visualization and propagation of uncertainty in BandMaths
  Pixel extraction tool
  Specific sensor processors:
  S3 OLCI Radiometry, S3 SLSTR PDU stitching
  AATSR/SLSTR Regridding
  Performs radiometric corrections on MERIS
  Optical water type classification based on atmospherically corrected reflectances
  FU (Forel-Ule) Classification used to derive the hue angle and FU value
  IdePix Processor: pixel classification
  FLH (Fluorescence Line Height) / MCI (Maximum Chlorophyll Index) retrieval
  FUB/WeW processor

## Slide 13: Sentinel-3 products
Sentinel-3 is an ocean and land mission and provides data continuity for the ERS, ENVISAT and SPOT-VGT satellites.
SENTINEL-3 makes use of multiple sensing instruments to accomplish its objectives:
SLSTR (Sea and Land Surface Temperature Radiometer)
OLCI (Ocean and Land Colour Instrument)
SRAL (SAR Altimeter)
DORIS (Doppler Orbitography and Radiopositioning Integrated by Satellite)
MWR (Microwave Radiometer)

## Slide 14: Access to Sentinels data
The Copernicus Open Access Hub provides complete, free and open access to Sentinel-1, Sentinel-2 and Sentinel-3 user products.
Go to https://scihub.copernicus.eu/

## Slide 15: Sentinel-1 level 1 GRDH
Available products
Level 0 (L0-RAW)
Level 1 Ground Range Detected, Multi-Looked, projected to ground range using Earth ellipsoid model WGS84- Medium Resolution (L1-GRDM) and High Resolution (L1-GRDH)
Level 1 Single-Look Complex (L1-SLC)
Level 2 Ocean (L2-OCN)
REMEMBER
In GRD data
Ground range coordinates are the slant range coordinates projected onto the ellipsoid of the Earth.
Pixel values represent detected amplitude – the power of reflected signal which depends on the surface scattering characteristics
Phase information is lost.
The resulting product has approximately square resolution pixels and square pixel spacing with reduced speckle at a cost of reduced spatial resolution.

## Slide 17: Sentinel-1 data acquisition
Terrain Observation
by Progressive Scans
(TOPS)

## Slide 18: Sentinel-1 level-1 SLC
Bursted IW SLC
TOPSAR Split to choose a subswath and bursts for the AOI

## Slide 19: Example for SAR data usage in SNAP
Sentinel-1 GRDH
File/Open Product/S1A_IW_GRDH_1SDV_20151003…
Expand the product in Product Explorer and view the list of bands and metadata
Inspect the image in the World View, main window, navigation and Color Manipulation windows
Subset the image to the AOI
Sentinel-1 SLC
File/Open Product/S1A_IW_SLC__1SDV_20151003…. metadata, bands, image inspection
Expand the product in Product Explorer and view the list of bands and metadata
Inspect the image in the World View, main window