## Slide 1
Pr. Pierre Defourny / Dr. Julien Radoux – UCLouvain, Belgium
Quality control of optical time series
and
temporal features computation

## Slide 2: Making good use of large time series
At least one image every 5 days
 more than 70 images per year
Consistency of the optical signal is a key
 We will focus on three questions
  Are images usable or not ?
    Fully cloudy images are discarded by preprocessing
  How to check the quality of the time series ?
    Cloud/cloud shadow flag
    Atmospheric corrections
  How to extract meaningfull information ?
    Phenology metrics

## Slide 3: Visual check is useful, but strenuous
OK
OK
Completely cloudy
(image skipped by preprocessor)
Partly cloudy
Poor radiometry

## Slide 4: Automated quality check of reflectance
Use of pseudo-invariant targets
Examples:
  Desert
  Water
  Impervious surfaces
  Salt flats
  Evergreen forests
  …
Make sure that they are really invariance in YOUR area

## Slide 5: Temporal metrics to capture the time series info
Max. positive
slope
Fastest growth of vegetation
Max. negative
slope
Maximum NDVI
(average of 3 max.)
Maximum Red
(average of 3 max.)
Minimum NDVI
(average of 3 max.)
4
5
1
3
2
NDVI
Time
Fast reduction of
vegetation
Maximum green
biomass
Bare soil at sowing preparation
Harvested crop or
non green residues
Example of specific set of metrics (features) designed for crop monitoring
(Matton et al., 2015, Waldner et al., 2016, Lambert et al., 2016)
First by pixels
Then by parcels

## Slide 6: Open your Jupyter notebook
You have a paper copy of the exercise
Interactive exercise is written in a Jupyter notebook
Double click on jupyter shortcut on your desktop
Load the notebook located in
/mnt/upload2/trainme/DATA/sessions/2_temporal_features/
jupyter_notebook/TrainingESA_TimeSeries_v2.ipynb