## Slide 1
Synthetic Aperture Radar Tomography – practical course
Timo Balz, Stefano Tebaldini, Laurent Ferro-Famil
测绘遥感信息工程国家重点实验室
State Key Laboratory of Information Engineering in Surveying, Mapping and Remote Sensing

## Slide 2
TomoSAR_Main.m
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% DEMONSTRATIVE TOMOGRAPHIC SAR PROCESSING FOR FOREST ANALYSIS
% AUTHOR: STEFANO TEBALDINI, POLITECNICO DI MILANO
% EMAIL: stefano.tebaldini@polimi.it
% TEL: +390223993614
%
% THE FOLLOWING SCRIPT AND ALL RELATED SCRIPTS/FUNCTIONS AND DATA ARE INTENDED AS
% MATERIAL FOR THE TOMOSAR TRAINING COURSE HELD IN BEIJING IN FEBRUARY 2015
% BY LAURENT FERRO-FAMIL AND STEFANO TEBALDINI
%
% THIS SOFTWARE WAS DEVELOPED AND TESTED USING MATLAB R2011b
%
% SAR DATA USED IN THIS SCRIPT ARE PART OF THE SAR DATA-SET ACQUIRED BY DLR
% IN 2008 IN THE FRAME OF THE ESA CAMPAIGN BIOSAR 2008
% DATA FOCUSING, COREGISTRATION, PHASE FLATTENING, AND GENERATION OF KZ
% MAPS WERE CARRIED OUT BY DLR.
% DATA PHASE CALIBRATION WAS CARRIED OUT BY THE AUTHOR
%
% TERRAIN ELEVATION DATA USED IN THIS SCRIPT ARE EXTRACTED FROM
% THE LIDAR DATA-SET ACQUIRED BY THE SWEDISH DEFENCE RESEARCH AGENCY (FOI)
% AND HILDUR AND SVEN WINQUIST'S FOUNDATION IN THE FRAME OF THE ESA
% CAMPAIGN BIOSAR 2008
% PROCESSING OF LIDAR DATA AND PROJECTION ONTO SAR GEOMETRY WAS CARRIED OUT
% BY THE AUTHOR
%
% YOU ARE WELCOME TO ADDRESS ME QUESTIONS/COMMENTS/CORRECTIONS AT
% stefano.tebaldini@polimi.it
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%

## Slide 3
Ambiguities

## Slide 5
TomoSAR principle

## Slide 6
TomoSAR principle

## Slide 7
TomoSAR principle

## Slide 8
TomoSAR principle

## Slide 9
TomoSAR principle

## Slide 10
Why multiple baselines?
  Because: more equations!
  Increased robustness against disturbances (temporal decorrelation…)
  and/or relaxation of hypotheses required in the single baseline case
  more unknowns are available to characterize the vertical structure of the scene
N=2
N=3
…
N is large
Backscattered Power
z
z
z
Top Height, Extinction
Mean, Std, Skewness
Tomographic Reconstruction
Backscattered Power
Backscattered Power
MB allow to pass from model-based inversion to full tomographic reconstruction
Tebaldini & Rocca

## Slide 11
ground range
height
azimuth
Slant range
resolution cell
Replicas
θ
Height of ambiguity
Normal baseline
Rationale: Form a 2D synthetic aperture by collecting multiple SAR acquisitions acquired along parallel flight lines
  Vertical resolution  total normal baseline span
  Vertical ambiguity  normal baseline spacing
Multi-baseline (MB) systems:
Multiple pass systems:
  airborne and spaceborne SARs
Multiple antenna systems:
  ground based Radars
MB campaigns involve:
Higher costs:
  spaceborne: ≈ x 1
  ground based: ≈ x N
More sophisticated processing:
  see single vs multi-baseline InSAR…
Source:
Tebaldini & Rocca

## Slide 12
ground range
height
azimuth
Slant range
resolution cell
Replicas
θ
Height of ambiguity
Normal baseline
Rationale: Form a 2D synthetic aperture by collecting multiple SAR acquisitions acquired along parallel flight lines
  Vertical resolution  total normal baseline span
  Vertical ambiguity  normal baseline spacing
Multi-baseline (MB) systems:
Multiple pass systems:
  airborne and spaceborne SARs
Multiple antenna systems:
  ground based Radars
MB campaigns involve:
Higher costs:
  spaceborne: ≈ x 1
  ground based: ≈ x N
More sophisticated processing:
  see single vs multi-baseline InSAR…
Source: Tebaldini & Rocca
Tomographic SAR

## Slide 13
Track 1
Reference Track (Master)
Track n
azimuth
height
ground range
slant range
θ
π/2
cross range
Flight tracks orthogonal
to the blackboard
Master
Normal baseline for the n-th track
Track n
azimuth
slant range
cross range
baseline vector for the n-th track
Multiple baselines  Illumination from multiple points of view
By collecting several baselines it is possible to synthesize an antenna along the cross range direction as well
3D focusing is possible in the coordinate system: slant range, azimuth, cross range
Source: Tebaldini & Rocca
Basic concepts

## Slide 14
slant range, r
cross range, v
Track 1
Track n
Track N
ground range
height
azimuth
Baseline aperture
Resolution is determined by pulse bandwidth along the slant range direction, and by the lengths of the synthetic apertures in the azimuth and cross range directions
The SAR resolution cell is split into multiple layers, according to baseline aperture
B: pulse bandwidth
Av: baseline aperture
Ax: azimuth aperture
λ: carrier wavelength
height
ground range
Δr
Δv
For most systems:
Δv >> Δr, Δx
SAR Resolution Cell
Tomographic Res. Cell
Source: Tebaldini & Rocca
Basic concepts

## Slide 15
Ice
y [m]
z [m]
0
1
2
3
4
5
6
7
-2
-1.5
-1
-0.5
0
0.5
Snow
height [m]
200
600
1000
1400
1800
2200
-10
0
10
20
30
40
50
60
slant range [m]
Forested areas
Man-made structures
Urban scenarios
Source: Tebaldini & Rocca
TomoSAR gives access to the 3D structure

## Slide 16
Foliage penetration
Biomass estimation
Polarimetric TomoSAR over Vegetation

## Slide 17
Finite number of scatterers
Urban TomoSAR

## Slide 18
Irregular sampling &
Limited acquisitions
Orbit uncertainties &
tropospheric delay
Δb
r
s
= low resolution in s
TomoSAR principle

## Slide 19
where
so, gn is the Fourier transformation of at position
TomoSAR as spectral estimation problem

## Slide 20
The focused SAR image from the nth pass of a specific cell is nothing else but the Fourier Transfer of the reflectivity function in the elevation direction at the position fn.
TomoSAR basics

## Slide 21
The expected resolution in elevation depends on the slant-range r and the aperture size in elevation
The extent of the illuminated objects and therefore the limits of the extent in elevation s depends on r, , and the resolution in range . In the spaceborne case, with large slant-range r, this is seldom a limitation (see Zhu & Bamler, 2010).
TomoSAR basics

## Slide 22
Using TomoSAR on a large area requires the removal of atmospheric effects
This can be done using PS-InSAR
  However, this requires a large number of PS to be found
  Therefore, this works best in urban areas
PS-InSAR is used for pre-processing
Afterwards, TomoSAR can be used
PS-InSAR for pre-processing

## Slide 23
PS-InSAR

## Slide 24
Import
Selection of the master image
Co-Registration
    Typically to a single-master
Interferogram processing
    Not in every implementation. Several PS-InSAR implementations only use the phases of the PS candidates
PS candidates selection
APS estimation
    Typically on a subset of the PS candidates
PS point processing
Post-processing
Visualization
PS-InSAR steps

## Slide 25
Identical to the co-registration described in the InSAR section:
Registration accuracy < 0.2 pixel is required
  This requirement is even much higher during TOPS processing
Different methods available
    Based on the amplitude
    Based on complex data – searching maximal coherence
Slave images are resampled to the master image
Results need to be checked and the parameters may need to be adjusted
Image co-registration

## Slide 26
Classical way: amplitude dispersion index
Other possible ways, e.g. based on coherence
Be aware: amplitude dispersion index not ideal for TomoSAR, because the existence of several scatterers in a resolution cell can increase the index
PS candidate selection

## Slide 27
Example: SARProZ
APS estimation

## Slide 28
Beamforming:
inverse Fourier Transform; coarse spatial resolution; radiometrically consistent
Capon Spectral Estimator:
spatial resolution is greatly enhanced, at the expense of radiometric accuracy;
Methods based on the analysis of the Eigenstructure of R (MUSIC, ESPRIT…):
determination of the dominant scatterering centers; mostly suited for urban scenarios
Methods based on sectorial information (Truncated SVD, PCT…):
optimal basis choice (e.g.: Legendre), depending on a-priori info about the scene vertical extent
Model based methods (NLS, COMET…):
model based; high radiometric accuracy; high computational burden; possible model mismatches
Compressive sensing:
localization of few scattering centers via L1 norm minimization; mostly suited for urban scenarios
Spectral estimators

## Slide 29
where
gn = complex value observed for the nth pass
= complex amplitude of kth scatterer
= elevation of kth scatterer
= number of available images
=noise
=number of scatterers inside a resolution cell
=frequency of sampled FT which depends on the baseline
Multiple scatterers

## Slide 30
Non-linear least-square estimation

## Slide 31
SVD on real data

## Slide 32
Selecting a statistical model for given data
Selecting the correct model is the model selection problem
too simple –
order too low
appropriate model
too complex –
order too high
Model selection

## Slide 33
Bayesian Information Criterion (BIC)
Akaike Information Criterion (AIC)
Minimum Description Length (MDL)
Model selection methods

## Slide 34
TomoSAR processing steps

## Slide 35
3D scatterer reconstruction

## Slide 36
SVD based methods
  SVD
  Truncated SVD (T-SVD)
  Wiener SVD
  Butterworth-SVD
Compressive Sensing based methods
  Basis Pursuit (BP)
  TWIST
Urban TomoSAR different methods

## Slide 37
Another solution to SAR tomography is by L1 norm minimization, which is also the core of compressive sensing:
The argument listed above can be stated by
where is a weighted value adjusted according to the noise level.
TWIST

## Slide 38
SAR tomography with compressive sensing
  (see Zhu, Xiaoxiang’s work in the references)
Often, TomoSAR with compressive sensing is based on Basis Pursuit (BP)
  Very high super-resolution
  However, time-consuming
Alternatively: Two-Step Iterative Shrinkage Thresholding (TWIST) for TomoSAR
  Very efficient
  Less super-resolution capability
TWIST

## Slide 39
When using TWIST, the least squares fitting is needed to calculate
Calculate according to
where is the normalization equation.
If
in which, are the weighting coefficients
TWIST

## Slide 40
(a) s_Sc1=-20m, s_Sc2=30m;
(b) s_Sc1=8m, s_Sc2=30m;
(c) s_Sc1=23m; s_Sc2=30m
TomoSAR: different methods

## Slide 41
TSVD
TWIST
BP
TSVD, Twist & BP

## Slide 42
red: single;
blue: double;
black: multi
柏林实验区
（a）TSVD
85 seconds
（b）TWIST
89 seconds
（c）BP
1378 seconds
TSVD, Twist & BP

## Slide 43
Extend the model to the time-domain and include an estimation of the deformation
  4D TomoSAR
Basically just an extension of the previously described method
  Including an additional dimension for the focusing
Can be further extended by including seasonal motion
  Sometimes called 5D TomoSAR
Differential TomoSAR

## Slide 44
Simulation results:
BSVD
TWIST
= for D-TomoSAR, the noise suppression gets even more important
D-TomoSAR

## Slide 45
Example: TSX stack from Las Vegas:
BSVD
TWIST
= clear result in TWIST
D-TomoSAR

## Slide 46
Due to the high computational demand for compressive sensing TomoSAR, the processing can be divided:
PS-InSAR for pre-processing – APS estimation
Basic TomoSAR processing for model estimation
Depending on the number of scatterers:
    One scatterer per resolution cell: use PS-InSAR for processing
    Two or more scatterer: use TomoSAR
Practical implementations

## Slide 47
Fusion of SAR imaging geodesy and TomoSAR
SAR imaging geodesy:
  Very high absolute geo-positioning capability of SAR
  Especially with TerraSAR-X due to the very precise orbit
  see Eineder et al, Cong et al, Balss et al….
The fusion allows getting precise absolute 3D positions
Geodetic SAR tomography

## Slide 48
from Zhu et al, 2016 – 3D absolute positioned TomoSAR point cloud from Berlin
from Zhu et al, 2016 – Amplitude of the seasonal motion derived from one stack
Geodetic SAR tomography

## Slide 49
  Reigber, A.; Moreira, A.; , "First demonstration of airborne SAR tomography using multibaseline L-band data," Geoscience and Remote Sensing, IEEE Transactions on , vol.38, no.5, pp.2142-2152, Sep 2000
  G. Fornaro, F. Serafino, and F. Soldovieri, “Three-dimensional focusing with multipass SAR data,” IEEE Trans. Geosci. Remote Sens., vol. 41, no. 3, pp. 507–517, Mar. 2003.
  F. Lombardini, “Differential tomography: a new framework for SAR interferometry,” IEEE Trans. Geosci. Remote Sens., vol. 43, no. 1, pp. 37–44, Jan. 2005.
  G. Fornaro and F. Serafino, “Imaging of Single and Double Scatterers in Urban Areas via SAR Tomography,” IEEE Trans. Geosci. Remote Sens., vol. 44, no. 12, pp. 3497–3505, Dec. 2006.
  F. Lombardini and M. Pardini, “3-D SAR Tomography: The Multibaseline Sector Interpolation Approach,” IEEE Geosci. Remote Sens. Lett., vol. 5, no. 4, pp. 630–634, Oct. 2008.
  G. Fornaro, D. Reale, and F. Serafino, “Four-Dimensional SAR Imaging for Height Estimation and Monitoring of Single and Double Scatterers,” IEEE Trans. Geosci. Remote Sens., vol. 47, no. 1, pp. 224–237, Jan. 2009.
  X. X. Zhu and R. Bamler, “Tomographic SAR Inversion by L1-Norm Regularization—The Compressive Sensing Approach,” IEEE Trans. Geosci. Remote Sens., vol. 48, no. 10, pp. 3839–3846, Oct. 2010.
  X. X. Zhu and R. Bamler, “Let’s Do the Time Warp: Multicomponent Nonlinear Motion Estimation in Differential SAR Tomography,” IEEE Geosci. Remote Sens. Lett., vol. 8, no. 4, pp. 735–739, 2011.
  X. X. Zhu and R. Bamler, “Very High Resolution Spaceborne SAR Tomography in Urban Environment,” IEEE Trans. Geosci. Remote Sens., vol. 48, no. 12, pp. 4296–4308, 2010.
  X. X. Zhu and R. Bamler, “Super-Resolution Power and Robustness of Compressive Sensing for Spectral Estimation With Application to Spaceborne Tomographic SAR,” IEEE Trans. Geosci. Remote Sens., vol. 50, no. 1, pp. 247–258, 2011.
  X. X. Zhu and R. Bamler, “Demonstration of Super-Resolution for Tomographic SAR Imaging in Urban Environment,” IEEE Trans. Geosci. Remote Sens., vol. 50, no. 8, pp. 3150–3157, Aug. 2012.
  F. Lombardini and M. Pardini, “Superresolution Differential Tomography: Experiments on Identification of Multiple Scatterers in Spaceborne SAR Data,” IEEE Trans. Geosci. Remote Sens., vol. 50, no. 4, pp. 1117–1129, 2012.
  D. Reale, G. Fornaro, and A. Pauciullo, “Extension of 4-D SAR Imaging to the Monitoring of Thermally Dilating Scatterers,” IEEE Trans. Geosci. Remote Sens., vol. 51, no. 12, pp. 5296–5306, 2013.
  G. Fornaro, A. Pauciullo, D. Reale, and S. Verde, “Multilook SAR Tomography for 3-D Reconstruction and Monitoring of Single Structures Applied to COSMO-SKYMED Data,” IEEE J. Sel. Top. Appl. Earth Obs. Remote Sens., vol. 7, no. 7, pp. 2776–2785, Jul. 2014.
  X. X. Zhu, S. Montazeri, C. Gisinger, R. F. Hanssen, and R. Bamler, “Geodetic SAR Tomography,” IEEE Trans. Geosci. Remote Sens., vol. 54, no. 1, pp. 18–35, Jan. 2016.
References

## Slide 50
Assuming typical airborne or spaceborne MB geometries, SAR Tomography can be formulated according to one simple principle:
yn(r,x) : SLC pixel in the n-th image
s(r,x,v): average complex reflectivity of the scene within the SAR 2D resolution cell at (r,x)
bn : normal baseline for the n-th image
λ : carrier wavelength
Each focused SLC SAR image is obtained as the Fourier Transform of the scene complex reflectivity along the cross-range coordinate
cross range, v
transmitted pulse
|s(r,x,v)|2
Δr
Radar Line of Sight
The cross-range distribution of the complex reflectivity can be retrieved through Fourier-based techniques
Source: Tebaldini & Rocca
Tomographic scene reconstruction

## Slide 51
Example: Tomographic reconstruction of a forest scenario
Contributions from volume backscattering
Contributions from ground backscattering
Contributions from ground-trunk interactions
|s(r,x,z)|2
cross range, v
transmitted pulse
|s(r,x,v)|2
height, z
Δr
Radar Line of Sight
Simulated Backscattered Power Distribution (BPD)
0
0.5
1
-10
0
10
20
30
40
height [m]
Simulated
0
0.1
0.2
-10
0
10
20
30
40
height [m]
Beamforming
0
0.2
0.4
-10
0
10
20
30
40
height [m]
Capon Spectrum
0
0.5
-10
0
10
20
30
40
height [m]
COMET - 2 Layers
BPD
Estimated BPD
Estimated BPD
Estimated BPD
N = 6
N = 12
N = 6
N = 12
N = 6
N = 12
Source:
Tebaldini &
Rocca
Tomographic scene reconstruction

## Slide 52
Track 1
Reference Track (Master)
Track n
Azimuth
Elevation
Ground range
Slant range
θ
π/2
Cross range
Source:
Tebaldini & Rocca
BIOMASS tomographic phase

## Slide 53
Radar Line of Sight
  A closer look…
Source: Rocca
Tomographic analysis: TropiSAR

## Slide 54
Radar Line of Sight
This resolution cell gathers contributions from terrain only.
=> Signal intensity in this cell is affected by terrain slope the same way as in traditional SAR images of bare surfaces
  A closer look…
Source: Rocca
Tomographic analysis: TropiSAR

## Slide 55
Radar Line of Sight
This cell is completely within the volume layer, independently on volume orientation w.r.t. the Radar LOS.
=> Signal intensity in this cell is independent of terrain slope
This resolution cell gathers contributions from terrain only.
=> Signal intensity in this cell is affected by terrain slope the same way as in traditional SAR images of bare surfaces
  A closer look…
Source: Rocca
Tomographic analysis: TropiSAR

## Slide 56
Radar Line of Sight
This cell is completely within the volume layer, independently on volume orientation w.r.t. the Radar LOS.
=> Signal intensity in this cell is independent of terrain slope
The scattering volume within cells at the boundaries of the vegetation layer depends on volume orientation w.r.t. the Radar LOS.
=> Signal intensity in this cell is affected by terrain slope in a similar way as the cell corresponding to the ground layer.
This resolution cell gathers contributions from terrain only.
=> Signal intensity in this cell is affected by terrain slope the same way as in traditional SAR images of bare surfaces
  A closer look…
Source: Rocca
Tomographic analysis: TropiSAR

## Slide 57
Co-polar signature at the ground layer reveals ground-trunk double bounce interactions dominate the signal from flat areas despite the presence of a 40 m dense tropical forest
Source: Rocca
Tomographic analysis: TropiSAR

## Slide 58
SAR tomography allows to map not only vertical forest structure but also biomass.
The scattering mechanisms at P-band in a very dense tropical forest:
It was found that scattering contributions from about 30 m above ground exhibit high sensitivity to forest biomass value ranging from 250 t/ha to 450 t/ha.
Ground scattering is strongly visible and double bounces in flat terrain topography are visible everywhere.
Volume scattering is significantly related to the high range biomass
Towards BIOMASS

## Slide 59
P-band SAR tomography
key tool to SEE through the forest
    suitable long wavelength to penetrate the dense forest layer
    key indicator to tropical forest biomass
GOAL: Study the temporal decorrelation of scattering mechanisms of the radar signal in a tropical forest as a function of height and polarization.
Orbit constraint: temporal decorrelation
    Revisit time ≥ 1 day in a sun synchronous satellite configuration
    Forest scattering changes with time
Forest temporal decorrelation

## Slide 60
Polarimetric and tomographic phenomenology of forests
  Reigber, A.; Moreira, A.; , "First demonstration of airborne SAR tomography using multibaseline L-band data," Geoscience and Remote Sensing, IEEE Transactions on , vol.38, no.5, pp.2142-2152, Sep 2000
  Mariotti d'Alessandro, M.; Tebaldini, S.; , "Phenomenology of P-Band Scattering From a Tropical Forest Through Three-Dimensional SAR Tomography," Geoscience and Remote Sensing Letters, IEEE , vol.9, no.3, pp.442-446, May 2012
  Frey, O.; Meier, E.; , "3-D Time-Domain SAR Imaging of a Forest Using Airborne Multibaseline Data at L- and P-Bands," Geoscience and Remote Sensing, IEEE Transactions on , vol.49, no.10, pp.3660-3664, Oct. 2011
Multi-layer optimization
  S. Sauer, L. Ferro-Famil, A. Reigber, E. Pottier, “Multi-aspect POL-InSAR 3D Urban Scene Reconstruction at L-Band”, Eusar 2008
  Y. Huang, L. Ferro-Famil, A. Reigber, “Under Foliage Object Imaging Using SAR Tomography
  and Polarimetric Spectral Estimators”, Eusar 2010
Coherence optimization
  M. Neumann, L. Ferro-Famil, A. Reigber, “Multibaseline Polarimetric SAR Interferometry Coherence Optimization”, IEEE Geoscience and Remote Sensing Letters, 2008
  E. Colin, C. Titin-Schnaider, W. Tabbara, “An Interferometric Coherence Optimization Method in Radar Polarimetry for High-Resolution Imagery”, IEEE Transactions on Geoscience and Remote Sensing, 2006
SKP decomposition: theory, algorithms and physical implications
  S. Tebaldini, “Algebraic Synthesis of Forest Scenarios from Multi-Baseline PolInSAR Data”, IEEE Transactions on Geoscience and Remote Sensing, 2009
  Tebaldini, S.; Rocca, F.; , "Multibaseline Polarimetric SAR Tomography of a Boreal Forest at P- and L-Bands," Geoscience and Remote Sensing, IEEE Transactions on , vol.50, no.1, pp.232-246, Jan. 2012
References

## Slide 61
Questions?
balz@whu.edu.cn