SURVEYS

4.0

#### SURVEYS

4.1	Traffic and Transport Surveys

Within the context of the Integrated Public Transport and Land Use Study in the Klang Valley, the prime purpose of surveys was to provide inputs into a transport model to be used to assess the impact of alternative networks. The transport model was then used to evaluate the various network configurations from the point of view of future transport demand. This important output, amongst other considerations determined the feasibility of the proposed transit network.

The traffic and transport surveys undertaken in this study involved collection of primary and secondary data on the existing conditions. This was necessary for the development of the public transport model. The collected data included transport inventories, transport data as well as socio-economic data. Following the development of the transport model for the base year, future demand was determined by the future socio-economic parameters as well as the committed future transport network. Consequently this determined the most desirable rail transit network for the Klang Valley.

4.1.1	Survey Types

Following a review of the available data, the need for additional traffic and transport information was determined. The types of traffic and transport surveys identified and conducted as part of this study were as follows:

- Bus Passenger Survey.

- Household Interview Survey (HIS)

- Stated Preference Survey

- Journey Time Survey

- Traffic Survey

  - Bus Passenger Survey

For the bus passenger survey, enumerators recorded the bus company, route number, estimated number of passenger seated or standing and the total number of seats available for the particular bus passing through the screenline. The general location of these screenlines are shown in Fig. 4.1.  A total of 43 stations have been surveyed for the bus passenger count survey as shown in Table 4.1. The summary of bus passenger count survey is shown in Table 4.2.

Table 4.1 – Bus Passenger Count Survey

| No. | Road |
| --- | --- |
|  | Jalan Kapar |
|  | Jalan Meru |
|  | Persiaran Raja Muda Musa |
|  | Jalan Langat |
|  | Jalan Kebun |
|  | Federal Highway FR2 near Padang Jawa |
|  | Persiaran Tengku Ampuan, Shah Alam |
|  | Persiaran Glen Marie, Shah Alam |
|  | Persiaran Sultan |
|  | Federal Highway FR2 before Subang Jaya exit |
|  | Lebuhraya Damasara-Puchong before Sunway Toll |
|  | Jalan Tujuan, Subang Jaya |
|  | Jalan Kewajipan, Subang Jaya |
|  | Jalan Subang (to Subang Airport) |
|  | Lebuhraya Damasara-Puchong near KDU |
|  | Jalan SS 2, Petaling Jaya |
|  | Jalan 222, Petaling Jaya |
|  | Federal Highway FR2 after Motorolla Int. |
|  | Jalan Puchong |
|  | Puchong-Sungai Besi Bypass Road |
|  | Jalan Templer, Petaling Jaya |
|  | Jalan Gasing, Petaling Jaya |
|  | Jalan Klang Lama, Kuala Lumpur |
|  | Federal Highway FR2 after Arch |
|  | Jalan Damasara, SPRINT |
|  | MRRII near Kepong |
|  | Jalan Kepong |
|  | Jalan Kuching |
|  | Jalan Gombak |
|  | Jalan Genting Klang |
|  | Jalan Ampang near MRRII |
|  | Jalan Cheras |
|  | Sungai Besi Road |
|  | KL-S’ban Highway before Toll |
|  | Jalan Bangsar, Kuala Lumpur |
|  | Jalan Syed Putra |
|  | Jalan Ipoh, Kuala Lumpur |
|  | Jalan Pahang, Kuala Lumpur |
|  | Jalan Ampang near Jalan Tun Razak |
|  | Jalan Kg. Pandan, Kuala Lumpur |
|  | Jalan Pudu, Kuala Lumpur |
|  | Jalan Loke Yew |
|  | Jalan Sungai Besi |

Fig. 4.1 - Screenlines

The data in Table 4.2 shows that the proportion of standing passengers is 17% compared to 93% seated passenger.  This means that the occupancy rate of passenger for buses is particularly high during the morning peak.

Table 4.2 : Summary of Bus Passenger Survey

| No. | Road | Inbound | Outbound | Total |
| --- | --- | --- | --- | --- |
|  |  | seat | stand | seat | stand | seat | stand |
|  | Jalan Kapar | 2617 | 80 | 3029 | 195 | 5646 | 275 |
|  | Jalan Meru | 521 | 0 | 741 | 51 | 1262 | 51 |
|  | Persiaran Raja Muda Musa | 3379 | 59 | 3519 | 60 | 6898 | 119 |
|  | Jalan Langat | 5518 | 297 | 6131 | 616 | 11649 | 913 |
|  | Jalan Kebun | 1931 | 47 | 1762 | 52 | 3693 | 99 |
|  | Federal Highway FR2 near Padang Jawa | 6316 | 65 | 7187 | 227 | 13503 | 292 |
|  | Persiaran Tengku Ampuan, Shah Alam | 477 | 32 | 758 | 0 | 1235 | 32 |
|  | Persiaran Glen Marie, Shah Alam | 133 | 0 | 239 | 9 | 372 | 9 |
|  | Persiaran Sultan | 1987 | 67 | 1533 | 306 | 3520 | 373 |
|  | Federal Highway FR2 before Subang Jaya exit | 8995 | 403 | 8150 | 444 | 17145 | 847 |
|  | Lebuhraya Damasara-Puchong before Sunway Toll | 2422 | 383 | 2522 | 489 | 4944 | 872 |
|  | Jalan Tujuan, Subang Jaya | 3756 | 194 | 921 | 104 | 4677 | 298 |
|  | Jalan Kewajipan, Subang Jaya | 5431 | 302 | 1503 | 227 | 6934 | 529 |
|  | Jalan Subang (to Subang Airport) | 1022 | 216 | 1007 | 214 | 2029 | 430 |
|  | Lebuhraya Damasara-Puchong near KDU | 3076 | 189 | 2307 | 59 | 5383 | 248 |
|  | Jalan SS 2, Petaling Jaya | 1502 | 22 | 1413 | 62 | 2915 | 84 |
|  | Jalan 222, Petaling Jaya | 1101 | 109 | 876 | 82 | 1977 | 191 |
|  | Federal Highway FR2 after Motorolla Int. | 13960 | 555 | 13641 | 1063 | 27601 | 1618 |
|  | Jalan Puchong | 5203 | 154 | 4968 | 284 | 10171 | 438 |
|  | Puchong-Sungai Besi Bypass Road | 308 | 0 | 0 | 0 | 308 | 0 |
|  | Jalan Templer, Petaling Jaya | 78 | 3 | 35 | 0 | 113 | 3 |
|  | Jalan Gasing, Petaling Jaya | 2225 | 0 | 2345 | 0 | 4570 | 0 |
|  | Jalan Klang Lama, Kuala Lumpur | 2910 | 348 | 2717 | 341 | 5627 | 689 |
|  | Federal Highway FR2 after Arch | 13529 | 123 | 3506 | 268 | 17035 | 391 |

Table 4.2 : Summary of Bus Passenger Survey (Cont.)

| No. | Road | Inbound | Outbound | Total |
| --- | --- | --- | --- | --- |
|  |  | seat | stand | seat | stand | seat | stand |
|  | Jalan Damasara, SPRINT | 1554 | 123 | 1726 | 92 | 3280 | 215 |
|  | MRRII near Kepong | 3250 | 66 | 3005 | 116 | 6255 | 182 |
|  | Jalan Kepong | 4618 | 85 | 5448 | 227 | 10066 | 312 |
|  | Jalan Kuching | 5461 | 341 | 6662 | 969 | 12123 | 1310 |
|  | Jalan Gombak | 4132 | 191 | 3519 | 164 | 7651 | 355 |
|  | Jalan Genting Klang | 4633 | 600 | 5654 | 727 | 10287 | 1327 |
|  | Jalan Ampang near MRRII | 9477 | 1264 | 8514 | 1102 | 17991 | 2366 |
|  | Jalan Cheras | 10992 | 1593 | 12815 | 1963 | 23807 | 3556 |
|  | Sungai Besi Road | 1022 | 117 | 860 | 106 | 1882 | 223 |
|  | KL-S’ban Highway before Toll | 12462 | 0 | 10774 | 21 | 23236 | 21 |
|  | Jalan Bangsar, Kuala Lumpur | 16555 | 1727 | 13823 | 1276 | 30378 | 3003 |
|  | Jalan Syed Putra | 6973 | 57 | 11958 | 407 | 18931 | 464 |
|  | Jalan Ipoh, Kuala Lumpur | 23803 | 2429 | 22121 | 2136 | 45924 | 4565 |
|  | Jalan Pahang, Kuala Lumpur | 15001 | 969 | 16831 | 1307 | 31832 | 2276 |
|  | Jalan Ampang near Jalan Tun Razak | 10375 | 1105 | 8682 | 1556 | 19057 | 2661 |
|  | Jalan Kg. Pandan, Kuala Lumpur | 3950 | 0 | 4728 | 0 | 8678 |  |
|  | Jalan Pudu, Kuala Lumpur | 24637 | 2068 | 22168 | 3130 | 46805 | 5198 |
|  | Jalan Loke Yew | 1253 | 0 | 3475 | 325 | 4278 | 325 |
|  | Jalan Sungai Besi | 1660 | 88 | 711 | 20 | 2371 | 108 |

4.3	Household Interview Surveys

The objective of household interview surveys is to ascertain the existing travel pattern in the study area. The information that was be obtained from this survey includes type of trips made (i.e. home based work trips, non-home based trips, etc.), type of vehicle owned, income group and traveling modes.

The result of the household data was used to develop the trips distribution pattern by trips purpose and trip production formulas in the study area. This survey also provides information on the socio-economic status of households / occupants and further provides a comprehensive data base of travel making patterns by all modes.

The distribution of the sample size between the various traffic zones was done in conjunction with the socio-economist, who ensured that the samples in these zones were homogenous. It was then established that at least the same type of information, as collected in the SMURT Study, would be required in this Survey. That is, besides household size, income, vehicle ownership and other household profile particulars, information on occupation, employment, income, travel mode for each working and non-working member of the household would need to be solicited.

In addition, for each member of the household over 7 years of age, a “person trip movement” for a particular day, would be recorded. The time of origin, destination, purpose of trip mode of travel (including intermediate transfer) for all trips done on that day was noted.

A sample size of 3,015 households was selected within the Klang Valley. They were essentially living quarters in the five regions and in proportion to the Klang Valley population distribution. To facilitate inter-regional comparisons within Klang Valley as well as to study commuter or transport patterns of households, within it, the five regions in the Study Area were sub-divided into 18 sub regions. Kuala Lumpur and Petaling which account for 55 percent of the total population of Klang Valley have seven and four sub-regions respectively.

The main findings of the household profile and the perception of those who commute using public transport systems are shown in this following section.

4.3.1	Household Information

a.	Total Number of Persons

The total number of persons in the sample of 3015 living quarters, selected from the five regions in Klang Valley, is 13,584 of this 51 percent is male and 49 percent female. Of the total population in the sample, 42 percent are in employment with the majority of the working persons being male (61 percent). The non-working group is equally large (41 percent) with the female members forming 61 percent of the total number. The total number of persons in the surveyed households is as shown in Table 4.3.

Table 4.3 : Total Number Of  Persons In Household In Klang Valley By Sex And Employment Status, 2003 (n=3015)

| Location | < 7 years | Working | Not Working | Total |
| --- | --- | --- | --- | --- |
|  | M | F | T | M | F | T | M | F | T | M | F | Total |
| Kuala Lumpur | 354 | 311 | 665 | 901 | 579 | 1480 | 604 | 957 | 1561 | 1859 | 1847 | 3706 |
| Gombak | 108 | 88 | 196 | 326 | 215 | 541 | 244 | 335 | 579 | 678 | 638 | 1316 |
| Ulu Langat | 55 | 59 | 114 | 202 | 135 | 337 | 120 | 201 | 321 | 377 | 395 | 772 |
| Petaling | 408 | 379 | 787 | 1200 | 810 | 2010 | 793 | 1155 | 1948 | 2401 | 2344 | 4745 |
| Klang | 296 | 302 | 598 | 813 | 499 | 1312 | 441 | 694 | 1135 | 1550 | 1495 | 3045 |
| Total Klang Valley | 1221 | 1139 | 2360 | 3442 | 2238 | 5680 | 2202 | 3342 | 5544 | 6865 | 6719 | 13584 |
|  | 17 % | 42 % | 41 % | 100 % |

Source:	Household Information Survey - HIS 1, 2003

Notes:	M = Male

F = Female

T = Total

b.	Monthly Household Income

A total of 2,992 households or 99 percent of the households surveyed reported total monthly household income ranging from “below RM 1,000”, “RM 1,000 to RM 2,000”, “RM 2,000 to RM 3,000”, RM 3,000 to RM 4,000” and “more than RM 5,000”. The monthly income by region and income groups is as shown in Table 4.4 below.

Table 4.4 : Proportion Of Households With Monthly Household Income

By Income Group And By Region, 2003 (%)

| Region | <RM1000 | RM1000-RM2000 | RM2000-RM3000 | RM3000-RM4000 | RM4000-RM5000 | >RM5000 | Total (%) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Kuala Lumpur | 9 | 24 | 17 | 13 | 10 | 27 | 100 |
| Gombak | 5 | 20 | 21 | 15 | 17 | 22 | 100 |
| Ulu Langat | 3 | 21 | 17 | 19 | 15 | 25 | 100 |
| Petaling | 6 | 13 | 15 | 16 | 16 | 34 | 100 |
| Klang | 7 | 28 | 22 | 16 | 13 | 14 | 100 |
| Klang Valley | 7 | 20 | 18 | 15 | 14 | 26 | 100 |

Source :	Household Information Survey - HIS 1, 2003

It is pertinent to note that only seven percent of the households in Klang Valley have a gross monthly household income of less than RM 1,000. One-fifth or 20 percent of the households are in the gross monthly household income group of RM 1,000 to RM 2,000. A relatively high proportion (26 percent) of the households mainly in Petaling (34 percent), Kuala Lumpur (27 percent), Ulu Langat (25 percent) reported monthly incomes of over RM 5,000. Two or more working members per household receiving relatively high incomes may be part of the reason for these reported high household incomes. Petaling, Kuala Lumpur and Ulu Langat being the hub of high economic activity in Klang Valley, and in the country as a whole, may have a relatively large proportion of households with high income earners.

It is also to be noted that over half (55 percent) of Klang Valley households receive incomes in excess of RM 3000 per month. It is only in Klang that a relatively low 43 percent of the households are in this high income bracket.

c.	Living Quarters

The majority of the living quarters surveyed are terrace houses (59 percent). Detached, semi-detached and flats covered were of equal proportions of 12 percent each. While a large proportion (71 percent) of the living quarters were owner occupied 29 percent were rented.  Rented living quarters were in higher proportions in Klang and Kuala Lumpur, each with 35 percent.

d.	Monthly Gross Income of Working Persons

Out of the total of 5,680 working persons listed in the 3015 households, 4,149 persons or 73 percent of them responded to the question on their monthly income. The number of responses within each region was sufficient enough to draw conclusions on the income status of working persons in the Study Area. Table 4.5 below shows the monthly income by regions of working persons in Klang Valley.

Table 4.5 : Proportion of  Working Persons By Monthly Income Groups

and by Region, 2003

| Region | <RM1000 | RM1000-RM2000 | RM2000-RM3000 | RM3000-RM4000 | RM4000-RM5000 | >RM5000 | Total |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Kuala Lumpur | 18 | 38 | 20 | 10 | 4 | 10 | 100 |
| Gombak | 10 | 38 | 30 | 12 | 4 | 6 | 100 |
| Ulu Langat | 18 | 37 | 22 | 12 | 5 | 6 | 100 |
| Petaling | 12 | 31 | 23 | 14 | 8 | 12 | 100 |
| Klang | 23 | 44 | 18 | 8 | 3 | 4 | 100 |
| Klang Valley | 16 | 37 | 22 | 11 | 5 | 9 | 100 |

Source :	Household Information Survey - HIS 1, 2003

The largest proportion (37 percent) of working persons in Klang Valley are in the RM 1,000 to RM 2000 income bracket. This is followed by 22 percent in the RM 2,000 to RM 3,000 income group. On the whole 25 percent of those working in Klang Valley are in the RM 3,000 and over income bracket. Petaling with 34 percent in this group has the highest proportion of high income earners in Klang Valley. Kuala Lumpur, Ulu Langat and Gombak with 24 percent, 23 percent and 22 percent, respectively are the other regions with relatively high income earners. It is again only in Klang that a high proportion, 85 percent, of the workers receive a monthly income of up to RM 3,000.

e.	Commuting By Car

In Klang Valley over 64 percent of the workers drive their own cars to work, 52 percent and another 12 percent commute to work in shared cars. The remaining 36 percent travel by other means of transport, either private or public. Table 4.6 below shows workers by region who commute to work by car.

Table 4.6 : Proportion of Workers Who Commute

by Car, by Region, 2003 (%)

| Region | Own car / Shared car | Other Modes | Total |
| --- | --- | --- | --- |
| Kuala Lumpur | 61 | 39 | 100 |
| Gombak | 79 | 21 | 100 |
| Ulu Langat | 63 | 37 | 100 |
| Petaling | 65 | 35 | 100 |
| Klang | 59 | 41 | 100 |
| Klang Valley | 64 | 36 | 100 |

Source : Household Information Survey - HIS 1, 2003

It appears that a larger proportion of workers in Gombak rely more on cars to travel to work than their fellow workers living in the other regions. A relatively larger proportion of workers in Klang use other modes of transport (41 percent) mainly motor cycles compared to the average Klang Valley workers (39 percent).

f.	Vehicle Ownership

Only 20 households or 0.7 percent of the sample do not own any form of transport vehicle. All the other households have at least one type of vehicle. Table 4.7 shows vehicle ownership by households by type and region.

Table 4.7 : Percentage of Vehicle Ownership by Households

in Klang Valley by Region and Type, 2003 (%)

| Region | Bicycle | Motorcycle | Car | Van | Bus | Lorry | None |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Kuala Lumpur | 30 | 45 | 81 | 5 | 0.4 | 1.0 | 1.0 |
| Gombak | 13 | 51 | 86 | 3 | 0.7 | 1.0 | 0.7 |
| Ulu Langat | 18 | 26 | 88 | 7 | 1.0 | 0.6 | - |
| Petaling | 3 | 42 | 88 | 4 | 0.5 | 2 | 0.4 |
| Klang | 39 | 53 | 80 | 5 | 1 | 3 | 0.9 |
| Klang Valley | 32 | 46 | 84 | 5 | 0.7 | 2 | 0.7 |

Source : Household Survey, HIS 1, 2003

Bicycle :  Ownership is relatively high among households in Kuala Lumpur and Klang but low in other regions especially in Petaling where only  3 percent reported to have this vehicle.

Motorcycle :   Klang followed by Gombak with 53 percent and 51 percent ownership respectively have the largest proportion of households owning motorcycles. This is reflective of the relatively low socio-economic and income levels of households in these regions.

Cars :  Motor car ownership in Klang Valley is relatively high at 84 percent. Car ownership in highest in Petaling, Ulu Langat and Gombak. 16 percent households in Klang Valley do not own cars. Klang (21 percent) and Kuala Lumpur (18 percent) have the highest proportion of households without cars. 44 percent of households in Klang Valley own one car with another 30 percent owning 2 cars per household. Households with three or more cars per household are relatively few and comprise only 10 percent. The majority of such households are found in Petaling (13 percent) and Kuala Lumpur (12 percent) followed by Gombak (10 percent), Klang (7 percent and Ulu Langat (8 percent) have the lowest number of households with three or more cars per household as shown in Table 4.8.

Van/bus/lorry:  These types of vehicles are almost absent in private households in Klang Valley, except for vans and lorries that are owned by some households mainly in Klang and Ulu Langat.

Table 4.8 : Proportion of Car Ownership By Number and Region, 2003 (%)

| Region | None | 1 | 2 | 3 | Total |
| --- | --- | --- | --- | --- | --- |
| Kuala Lumpur | 18 | 46 | 24 | 12 | 100 |
| Gombak | 14 | 48 | 28 | 10 | 100 |
| Ulu Langat | 12 | 54 | 26 | 8 | 100 |
| Petaling | 12 | 37 | 38 | 13 | 100 |
| Klang | 21 | 48 | 24 | 7 | 100 |
| Klang Valley | 16 | 44 | 30 | 10 | 100 |

Source:	Household Survey, HIS 1, 2003

4.4	Stated Preference Survey

Concurrently with the Household Information Survey, a Stated Preference Survey was also conducted on the selected sample of households. This questionnaire was directed to commuters who use private transport to travel to work or study.

4.4.1	Private Transport to Public Transport

Commuters who are currently using private transport – car or motorcycle – to travel to and from workplace or college were asked whether they would consider changing their mode of travel if a convenient public transport system – bus or rail – becomes available.

Close to two-thirds (65 percent) of the private transport users in Klang Valley are prepared to use public transport while only a third (35 percent) still wish to use their own vehicles to commute. Ulu Langat and Klang have a higher proportion of commuters wanting to use their cars/motorcycles to work or college. (see Table 4.9).

There is a high proportion of commuters in Gombak (71 percent), Petaling (67 percent) and Kuala Lumpur (64 percent) who are willing to make the switch to public transport if a convenient public transport system is made available.

Table 4.9 : Proportion of Private Transport Users

Willing to Use Public Transport System, 2003

| Region | Response (%) |
| --- | --- |
|  | Yes | No | Total |
| Kuala Lumpur | 64 | 36 | 100 |
| Gombak | 71 | 29 | 100 |
| Ulu Langat | 61 | 39 | 100 |
| Petaling | 67 | 33 | 100 |
| Klang | 62 | 38 | 100 |
| Klang Valley | 65 | 35 | 100 |

Source:	Stated Preference Survey – HIS 3B, 2003

4.4.2	Preference for Private Transport

Those commuters, the 35 percent from the above, who are unwilling to change to public transport, were asked what factors attracts them to continue using their own transport to work rather use the bus or rail. Invariably almost all responses, irrespective of region, indicated that private transportation is quicker (59 percent) and cheaper (37 percent) than public transport. Only a relatively small percentage stated additional reasons such as, that it is more comfortable (2 percent) and that they can avoid bad weather (2 percent). The response by region and factor is shown in Table 4.10 below.

Table 4.10 : Responses by Factors and by Region, 2003 (%)

| Region | Quicker | Cheaper | Avoid bad weather | More comfortable | Total |
| --- | --- | --- | --- | --- | --- |
| Kuala Lumpur | 58 | 35 | 3 | 4 | 100 |
| Gombak | 54 | 46 | - | - | 100 |
| Ulu Langat | 54 | 41 | 5 | - | 100 |
| Petaling | 65 | 32 | 1 | 2 | 100 |
| Klang | 57 | 39 | 1 | 3 | 100 |
| Klang Valley | 59 | 37 | 2 | 2 | 100 |

Source:	Stated Preference Survey – HIS 3B, 2003

It is clear that a large proportion of commuters of private transport, that is, almost three-fifths (59 percent) of them value getting to work on time and spending less travel time as very important reasons to use their cars to commute. This they believe they cannot get from public transport – at least not from the present public transport system.

4.4.3	Factors Likely to Induce Use of Public Transport

Perhaps exogenous factors such as increase in parking rates, difficulty in getting parking space, increase in fuel costs, traffic congestion, theft or damage to vehicles etc, are some of the factors that might induce the private transport users, to reconsider using public transport. In order to find out which of the factors the commuters feel has the greatest impact on them to induce them to use public transport, a list of nine factors were required by them to be ranked in order of importance or critical enough to induce change.

The response to each of the stated factors by region is as shown in Table 4.11 below.

Table 4.11 : Factors Considered Critical by Commuters by

Type and Region, 2003 (%)

| Region | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | Total |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Kuala Lumpur | 28 | 16 | 9 | 10 | 18 | 7 | 7 | 2 | 3 | 100 |
| Gombak | 57 | 11 | 3 | 3 | 11 | 7 | 4 | 1 | 3 | 100 |
| Ulu Langat | 33 | 18 | 19 | 7 | 9 | 3 | 5 | 3 | 3 | 100 |
| Petaling | 35 | 10 | 6 | 8 | 16 | 10 | 8 | 4 | 4 | 100 |
| Klang | 36 | 9 | 11 | 13 | 13 | 5 | 6 | 4 | 3 | 100 |
| Klang Valley | 35 | 12 | 9 | 9 | 15 | 7 | 7 | 3 | 3 | 100 |
| Rank | ( | ( | ( | ( | ( | ( | ( | ( | ( |  |

Source: Stated Preference Survey – HIS 3B, 2003

Notes:		1.  parking becomes difficult,

2.  parking rates are increased,

3. worry of theft/damage to car,

4. higher fuel/operating costs,

5. traffic congestion becomes severe,

6. quick access to rail/bus terminal becomes possible,

7. if journey time by rail/bus is less than by car,

8. if rail/bus fare are reasonably cheap and

9. if good feeder bus to rail stations are available.

For Klang Valley as a whole, the important factors, in descending order of importance that might induce private transport commuters to use public transport are as follows:-

| Rank | Factors | Percentage (%) |
| --- | --- | --- |
| 1 | Parking becoming difficult | 35 |
| 2 | Traffic congestion becomes severe | 15 |
| 3 | Parking rates are increased | 12 |
| 4 | Higher fuel/operating cost | 9 |
| 5 | Worry of theft/damage to car | 9 |
| 6 | Quick access to rail/bus terminal | 7 |
| 7 | Journey time by rail/bus less than by car | 7 |
| 8 | Rail/bus fares are reasonably cheap | 3 |
| 9 | Good feeder bus services to rail stations | 3 |
|  | Total | 100 |

Fig. 4.2 shows the factors in rank order of effectiveness.

Fig. 4.2: Factors Considered Critical by Commuters

by Type and Region, 2003 (%)

Source: 	Stated Preference Survey – HIS 3B, 2003

Notes:	1.  parking becomes difficult,

2.  parking rates are increased,

3. worry of theft/damage to car,

4. higher fuel/operating costs,

5. traffic congestion becomes severe,

6. quick access to rail/bus terminal becomes possible,

7. if journey time by rail/bus is less than by car,

8. if rail/bus fare are reasonably cheap and 9. if good feeder bus to rail stations are available.

The two most important factors that are reported to be most likely to induce the switch are parking becoming difficult (35%) and traffic congestion becoming severe (15%).  These are ranked as the top two factors that would induce the change.

It is pertinent to note however that cheap public transport fares (3%) and good feeder bus service to rail stations (3%) are the least likely factors to induce these commuters to make the switch from private to public transport.  Understandably other considerations such as, sending family members to work/school or if their work requires to use private cars overrides the benefits these latter incentives are likely to give.

It has to be stressed here however, that the ranking of the above factors are from the responses received from those commuting workers who wish to use their private transport and not from the entire sample population in the Klang Valley which would obviously welcome cheap public transport and good feeder bus services as incentives to use public transport.

4.4.4	Choice of Rail or Bus for Public Transport

The question posed to all private transport commuters as to which of the two modes – rail or bus – they would prefer if improved rail and bus systems are available, the majority in Klang Valley (69 percent) preferred to travel by rail while only 31 percent said they would prefer to travel by bus. Table 4.12 shows the choice of the mode of travel by region.

Table 4.12 : Choice of Mode by Region, 2003 (%)

| Region | Mode of Travel |
| --- | --- |
|  | Rail | Bus | Total |
| Kuala Lumpur | 72 | 28 | 100 |
| Gombak | 72 | 28 | 100 |
| Ulu Langat | 58 | 42 | 100 |
| Petaling | 77 | 23 | 100 |
| Klang | 55 | 45 | 100 |
| Klang Valley | 69 | 31 | 100 |

Source:	Stated Preference Survey – HIS 3B, 2003

Petaling (77 percent) followed by Kuala Lumpur (72 percent) and Gombak (72 percent) has the highest proportions of commuters wanting to use rail. There are relatively more commuters in Klang (45 percent) and Ulu Langat (42 percent) who prefer to travel by bus.

4.4.5	Type of Improvements Likely to Induce Commuters to Use Public Transport

The commuters who use private transport were asked what improvements to public transport would make them more likely to use it. Most of the commuters in Klang Valley were of the opinion that faster service, better connections and cheaper fares, ranked in that order, were the three important factors that would most likely induce them to use public transport. (See Table 4.13). Other factors such as more direct services, cleaner buses/trains and better reliability were considered less relevant or less important and are unlikely to induce commuters to change their mode of transport.

It is interesting to note, however, that commuters in Gombak consider better connections as the main factor (45 percent) that would make them use public transport. While 25 percent of commuters in Klang and 21 percent in Kuala Lumpur and Gombak feel cheaper fares is also a significant factor to induce them to use public transport.

The different responses within the regions to the improvements needed are as shown in the Fig. 4.3.

Table 4.13 : Improvements Likely to Induce Change

by Type and Region, 2003 (%)

| Region | Improvements Needed to Public Transport System | Total |
| --- | --- | --- |
|  | Better Connections | Faster Services | Cheaper Fares | More Direct Services | Cleaner Buses / Trains | Better Reliability |  |
| Kuala Lumpur | 25 | 40 | 21 | 6 | 4 | 4 | 100 |
| Gombak | 45 | 21 | 21 | 8 | 2 | 3 | 100 |
| Ulu Langat | 23 | 44 | 19 | 6 | 6 | 2 | 100 |
| Petaling | 31 | 39 | 15 | 8 | 4 | 3 | 100 |
| Klang | 26 | 38 | 25 | 5 | 2 | 4 | 100 |
| Klang Valley | 29 | 38 | 20 | 6 | 4 | 3 | 100 |

Source:	Stated Preference Survey – HIS 3B, 2003

Fig. 4.3 : Ranking of Improvements Within Region, 2003

4.5	Journey Time Survey

These are mainly to establish existing travel times on various corridors. It will provide a benchmark to calibrate the Transport model.  In addition, it provides a basis for comparing the improvements to the system with the proposed alternative routes.  There are 11 routes for journey time survey as shown in Fig. 4.4 and Table 4.14.

Table 4.14 - List of Travel Time Routes

| No. | Road Corridor |
| --- | --- |
| 1 | Federal Route 1 from Klang to Jalan Syed Putra |
| 2 | Jalan Pantai Dalam to Jalan Bangsar |
| 3 | Jalan Klang Lama to Taman Seputeh |
| 4 | Jalan Cheras to Jalan Loke Yew |
| 5 | Jalan Pudu |
| 6 | Jalan Tun Razak |
| 7 | Jalan Damansara to Jalan Semantan |
| 8 | Jalan Ampang |
| 9 | Jalan Pahang to Jalan Genting Klang |
| 10 | Jalan Kepong to Jalan Ipoh |
| 11 | Jalan Kuching from Batu Caves to Bank Negara |

A summary of the travel time survey results for the routes in the regional context is given in Table 4.15.

Based on the data shown, the average time taken to travel for most journeys is long and travel speed low. This  is primarily due to the high volume of traffic on the routes.

Figure 4.4 : Travel Time Survey Routes

Table 4.15 - Summary of Travel Time Survey for Regional Routes

| Route | Distance (km) | Inbound | Outbound |
| --- | --- | --- | --- |
|  |  | Time (s) | Average Speed (kph) | Time (s) | Average Speed (kph) |
| 1 | 25.6 | 4200 | 21.9 | 3600 | 25.6 |
| 2 | 6.4 | 1920 | 12.0 | 1020 | 22.6 |
| 3 | 6.8 | 3000 | 8.1 | 3420 | 7.1 |
| 4 | 24.3 | 3900 | 22.4 | 2700 | 32.4 |
| 5 | 7.6 | 4080 | 6.7 | 4440 | 6.1 |
| 6 | 12.5 | 900 | 50 | 1440 | 31.2 |
| 7 | 13.4 | 1800 | 26.8 | 3660 | 13.2 |
| 8 | 18.2 | 4440 | 14.8 | 2160 | 30.3 |
| 9 | 19.1 | 3240 | 21.2 | 1320 | 52 |
| 10 | 21.3 | 2520 | 30.4 | 2100 | 36.5 |
| 11 | 25.4 | 3600 | 25.4 | 1680 | 54.4 |

  - Traffic Surveys

These were conducted to establish existing traffic demand at selected screenline locations within the study area. The traffic surveys consisted of bus passenger count surveys and classified vehicle count surveys. The traffic surveys were conducted on a typical weekday and started at 6:00 am and finished at 10:00pm in the evening, covering a period of 16 hours. For the classified vehicle count, five vehicle categories i.e. cars/taxis, motorcycles, light trucks, heavy trucks and buses were surveyed. Data was recorded every 15 minutes. Classified vehicle were conducted on Federal Routes, State Roads and Local Roads only. The location of these traffic survey stations are listed in Table 4.16, while Fig. 4.5 shows the location of the Traffic Surveys.

Table 4.16 -  List of Screenline Survey Stations

| No. | Road |
| --- | --- |
|  | Jalan Kapar |
|  | Jalan Meru |
|  | Persiaran Raja Muda Musa |
|  | Jalan Langat |
|  | Jalan Kebun |
|  | NKVE before Bukit Raja Toll |
|  | Federal Highway FR2 near Padang Jawa |
|  | Shah Alam Expresway near Bukit Kemuning |
|  | Persiaran Tengku Ampuan, Shah Alam |
|  | Persiaran Glen Marie, Shah Alam |
|  | NKVE after Subang Toll |
|  | Jalan Glenmarie |

Table 4.16 -  List of Screenline Survey Stations (Cont.)

| No. | Road |
| --- | --- |
|  | Federal Highway FR2 before Subang Jaya exit |
|  | Shah Alam Expresway before Subang Jaya exit |
|  | Lebuhraya Damasara-Puchong before Sunway Toll |
|  | Jalan Tujuan, Subang Jaya |
|  | Jalan Kewajipan, Subang Jaya |
|  | Jalan Subang (to Subang Airport) |
|  | Lebuhraya Damasara-Puchong near KDU |
|  | Jalan SS 2, Petaling Jaya |
|  | Jalan 222, Petaling Jaya |
|  | Federal Highway FR2 after Motorolla Int. |
|  | Shah Alam Expresway after Puchong Jaya |
|  | Jalan Puchong |
|  | Puchong-Sungai Besi Bypass Road |
|  | Jalan Templer, Petaling Jaya |
|  | Jalan Gasing, Petaling Jaya |
|  | Jalan Klang Lama, Kuala Lumpur |
|  | Federal Highway FR2 after Arch |
|  | MRRII near Kepong |
|  | Jalan Kepong |
|  | Jalan Kuching |
|  | Jalan Gombak |
|  | Jalan Genting Klang |
|  | Elevated Highway, Ampang |
|  | Jalan Ampang near MRRII |
|  | Jalan Cheras |
|  | East-West Link |
|  | Sungai Besi Road |
|  | KL-S’ban Highway before Toll |
|  | Jalan Bangsar, Kuala Lumpur |
|  | Jalan Syed Putra |
|  | Jalan Ipoh, Kuala Lumpur |
|  | Jalan Pahang, Kuala Lumpur |
|  | Jalan Ampang near Jalan Tun Razak |
|  | Jalan Kg. Pandan, Kuala Lumpur |
|  | Jalan Pudu, Kuala Lumpur |
|  | Jalan Loke Yew |
|  | Jalan Sungai Besi |

Figure 4.5 - Locations of the Screen Line Survey Stations

The summary of the traffic volumes across the screen-lines is illustrated in Table 4.17.

Table 4.17 : Traffic Volumes at Screen-Lines

| No. | Location | Inbound | Outbound | TOTAL |
| --- | --- | --- | --- | --- |
|  | Jalan Kapar | 20530 | 22320 | 42850 |
|  | Jalan Meru | 28556 | 26344 | 54900 |
|  | Persiaran Raja Muda Musa | 38567 | 42179 | 80746 |
|  | Jalan Langat | 28332 | 30512 | 58844 |
|  | Jalan Kebun | 16235 | 16876 | 33111 |
|  | NKVE before Bukit Raja Toll | 25324 | 21164 | 46488 |
|  | Federal Highway FR2 near Padang Jawa | 44976 | 43085 | 88061 |
|  | Shah Alam Expresway near Bukit Kemuning | 18412 | 16304 | 34716 |
|  | Persiaran Tengku Ampuan, Shah Alam | 14392 | 16962 | 31354 |
|  | Persiaran Glen Marie, Shah Alam | 35966 | 34715 | 70681 |
|  | NKVE after Subang Toll | 34041 | 30636 | 64677 |
|  | Pesiaran Sultan | 23542 | 24397 | 47939 |
|  | Federal Highway FR2 before Subang Jaya exit | 75002 | 63124 | 138126 |
|  | Shah Alam Expresway before Subang Jaya exit | 24525 | 22912 | 47437 |
|  | Lebuhraya Damasara-Puchong before Sunway Toll | 38662 | 35689 | 74351 |
|  | Jalan Tujuan, Subang Jaya | 55432 | 36349 | 91781 |
|  | Jalan Kewajipan, Subang Jaya | 27088 | 25651 | 52739 |
|  | Jalan Subang (to Subang Airport) | 28628 | 27645 | 56273 |
|  | Lebuhraya Damasara-Puchong near KDU | 34917 | 34638 | 69555 |
|  | Jalan SS 2, Petaling Jaya | 24574 | 20887 | 45461 |
|  | Jalan 222, Petaling Jaya | 20437 | 16870 | 37307 |
|  | Federal Highway FR2 after Motorolla Int. | 84769 | 83434 | 168203 |
|  | Shah Alam Expresway after Puchong Jaya | 13662 | 12554 | 26216 |
|  | Jalan Puchong | 22306 | 19860 | 42166 |
|  | Puchong-Sungai Besi Bypass Road | 37814 | 34559 | 72373 |
|  | Jalan Templer, Petaling Jaya | 29820 | 28602 | 58422 |
|  | Jalan Gasing, Petaling Jaya | 15173 | 23067 | 38240 |
|  | Jalan Klang Lama, Kuala Lumpur | 46697 | 41320 | 88017 |
|  | Federal Highway FR2 after Arch | 107831 | 99119 | 206950 |
|  | MRRII near Kepong | 35517 | 35675 | 71192 |
|  | Jalan Kepong | 55876 | 55277 | 111153 |
|  | Jalan Kuching | 109589 | 101160 | 210749 |
|  | Jalan Gombak | 11889 | 15256 | 27145 |

Table 4.17 : Traffic Volumes at Screen-Lines(Cont.)

| No. | Location | Inbound | Outbound | TOTAL |
| --- | --- | --- | --- | --- |
|  | Jalan Genting Klang | 30502 | 37366 | 67868 |
|  | Elevated Highway, Ampang | 18254 | 15549 | 33803 |
|  | Jalan Ampang near MRRII | 33770 | 32576 | 66346 |
|  | Jalan Cheras | 47057 | 46827 | 93884 |
|  | East-West Link | 34074 | 37760 | 71834 |
|  | Sungai Besi Road | 34612 | 31832 | 66444 |
|  | KL-S’ban Highway before Toll | 72325 | 75144 | 147469 |
|  | Jalan Bangsar, Kuala Lumpur | 50342 | 52102 | 102444 |
|  | Jalan Syed Putra | 82622 | 81319 | 163941 |
|  | Jalan Ipoh, Kuala Lumpur | 164384 | 151740 | 316124 |
|  | Jalan Pahang, Kuala Lumpur | 40048 | 59378 | 99426 |
|  | Jalan Ampang near Jalan Tun Razak | 32196 | 30687 | 62883 |
|  | Jalan Kg. Pandan, Kuala Lumpur | 25818 | 26941 | 52759 |
|  | Jalan Pudu, Kuala Lumpur | 37923 | 36943 | 74866 |
|  | Jalan Loke Yew | 133668 | 132685 | 266353 |
|  | Jalan Sungai Besi | 181585 | 180198 | 361783 |

    - Traffic Volumes

The traffic composition during the screen-line survey was determined based on the same vehicle classification as the other traffic surveys. The modal split obtained from the survey data is illustrated in Table 4.18. It is quite apparent that private cars comprise the majority of the vehicles in the traffic stream at all screen-line locations (between 35% to 54% depending on location and direction). This is followed by motorcycles that make up between 24% to 40% of the traffic.

Table 4.18 – Traffic Volume (Inbound)

| No. | Road | Car | Lorry (mediums) | Lorry (>3axles) | Bus | Motorcycle |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Jalan Kapar | 11,726 | 2,464 | 1,419 | 430 | 4,491 |
| 2 | Jalan Meru | 20,274 | 3,099 | 827 | 216 | 4,140 |
| 3 | Persiaran Raja Muda Musa | 30,390 | 1,746 | 2,039 | 778 | 3,614 |
| 4 | Jalan Langat | 21,701 | 2,415 | 753 | 488 | 2,975 |
| 5 | Jalan Kebun | 9,758 | 1,596 | 653 | 346 | 3,882 |
| 6 | NKVE before Bukit Raja Toll | 19,748 | 1,428 | 1,337 | 213 | 2,598 |
| 7 | Federal Highway FR2 near Padang Jawa | 1266 | 836 | 779 | 4089 | 1266 |
| 8 | Shah Alam Expresway near Bukit Kemuning | 13,065 | 1,261 | 1,891 | 143 | 2052 |
| 9 | Persiaran Tengku Ampuan, Shah Alam | 12,323 | 253 | 48 | 140 | 1,628 |
| 10 | Persiaran Glen Marie, Shah Alam | 27,801 | 1,397 | 1,958 | 413 | 4,397 |
| 11 | NKVE after Subang Toll | 29805 | 686 | 383 | 56 | 3111 |
| 12 | Pesiaran Sultan | 18,674 | 1,019 | 14 | 158 | 3,677 |
| 13 | Federal Highway FR2 before Subang Jaya exit | 53,716 | 4,050 | 1,373 | 1,365 | 14,498 |
| 14 | Shah Alam Expresway before Subang Jaya exit | 20,423 | 1,027 | 715 | 122 | 2,238 |
| 15 | Lebuhraya Damasara-Puchong before Sunway Toll | 33,695 | 906 | 427 | 119 | 3,515 |
| 16 | Jalan Tujuan, Subang Jaya | 29,375 | 1,337 | 267 | 159 | 5,211 |
| 17 | Jalan Kewajipan, Subang Jaya | 21,385 | 308 | 856 | 164 | 2,938 |
| 18 | Jalan Subang (to Subang Airport) | 22,423 | 947 | 693 | 467 | 4,098 |
| 19 | Lebuhraya Damasara-Puchong near KDU | 30,253 | 872 | 495 | 76 | 3,221 |
| 20 | Jalan SS 2, Petaling Jaya | 17,448 | 192 | 1,324 | 125 | 1,798 |

Table 4.18 – Traffic Volume (Inbound) (Cont.)

| No. | Road | Car | Lorry (mediums) | Lorry (>3axles) | Bus | Motorcycle |
| --- | --- | --- | --- | --- | --- | --- |
| 21 | Jalan 222, Petaling Jaya | 12,983 | 742 | 83 | 79 | 2,983 |
| 22 | Federal Highway FR2 after Motorolla Int. | 64857 | 1,866 | 508 | 2,035 | 15,503 |
| 23 | Shah Alam Expresway after Puchong Jaya | 11644 | 400 | 327 | 41 | 1,250 |
| 24 | Jalan Puchong | 15,112 | 509 | 473 | 320 | 3,446 |
| 25 | Puchong-Sungai Besi Bypass Road | 32,038 | 1,141 | 1,527 | 265 | 2,843 |
| 26 | Jalan Templer, Petaling Jaya | 18,545 | 630 | 18 | 127 | 3,747 |
| 27 | Jalan Gasing, Petaling Jaya | 11,421 | 12,903 | 879 | 770 | 3,847 |
| 28 | Jalan Klang Lama, Kuala Lumpur | 36,282 | 1,170 | 3,113 | 403 | 5,729 |
| 29 | Federal Highway FR2 after Arch | 76966 | 2280 | 743 | 2161 | 16969 |
| 30 | MRRII near Kepong | 25,320 | 3,874 | 1,035 | 271 | 5,175 |
| 31 | Jalan Kepong | 41432 | 2699 | 458 | 1168 | 10119 |
| 32 | Jalan Kuching | 80044 | 5359 | 1238 | 2356 | 20592 |
| 33 | Jalan Gombak | 7,412 | 878 | 204 | 480 | 2,915 |
| 34 | Jalan Genting Klang | 27,741 | 404 | 2,120 | 403 | 6,698 |
| 35 | Elevated Highway, Ampang | 18,182 | 26 | 2 | 44 | 0 |
| 36 | Jalan Ampang near MRRII | 21,790 | 1,252 | 171 | 672 | 9,885 |
| 37 | Jalan Cheras | 30000 | 833 | 8 | 591 | 15625 |
| 38 | East-West Link | 29,387 | 816 |  | 46 | 3825 |
| 39 | Sungai Besi Road | 30,036 | 765 | 411 | 199 | 3,201 |
| 40 | KL-S’ban Highway before Toll | 32,798 | 1,134 | 683 | 828 | 36,882 |
| 41 | Jalan Bangsar, Kuala Lumpur | 32,538 | 3,774 | 280 | 1,520 | 13,990 |
| 42 | Jalan Syed Putra | 67000 | 1689 | 333 | 822 | 12778 |
| 43 | Jalan Ipoh, Kuala Lumpur | 122693 | 5610 | 145 | 3305 | 32631 |
| 44 | Jalan Pahang, Kuala Lumpur | 41,460 | 4,605 | 204 | 974 | 12,135 |
| 45 | Jalan Ampang near Jalan Tun Razak | 21,309 | 604 | 62 | 632 | 9,589 |
| 46 | Jalan Kg. Pandan, Kuala Lumpur | 19,961 | 282 | 1,031 | 237 | 5,430 |
| 47 | Jalan Pudu, Kuala Lumpur | 28800 | 608 | 64 | 1411 | 7040 |
| 48 | Jalan Loke Yew | 86667 | 5167 | 67 | 100 | 41667 |
| 49 | Jalan Sungai Besi | 12667 | 998 | 1920 | 31000 | 12667 |

Table 4.19 – Traffic Volume (Outbound)

| No. | Road | Car | Lorry (mediums) | Lorry (>3axles) | Bus | Motorcycle |
| --- | --- | --- | --- | --- | --- | --- |
|  | Jalan Kapar | 12,464 | 2,713 | 1,965 | 423 | 4,755 |
|  | Jalan Meru | 18,990 | 1,913 | 758 | 188 | 4,495 |
|  | Persiaran Raja Muda Musa | 33,932 | 1,459 | 1,852 | 696 | 4,240 |
|  | Jalan Langat | 25,855 | 1,355 | 411 | 456 | 2,435 |
|  | Jalan Kebun | 9,829 | 1,654 | 722 | 388 | 4,283 |
|  | NKVE before Bukit Raja Toll | 16,156 | 1,167 | 1,093 | 181 | 2,567 |
|  | Federal Highway FR2 near Padang Jawa | 36,516 | 1,101 | 787 | 710 | 3971 |
|  | Shah Alam Expresway near Bukit Kemuning | 11,355 | 1,211 | 1,711 | 133 | 1894 |
|  | Persiaran Tengku Ampuan, Shah Alam | 14,236 | 517 | 26 | 132 | 2,051 |
|  | Persiaran Glen Marie, Shah Alam | 26,941 | 1,043 | 2,268 | 413 | 4,050 |
|  | NKVE after Subang Toll | 26824 | 617 | 345 | 50 | 2800 |
|  | Pesiaran Sultan | 20890 | 429 | 81 | 237 | 2,760 |
|  | Federal Highway FR2 before Subang Jaya exit | 44,843 | 3,604 | 1,427 | 1,130 | 12,120 |
|  | Shah Alam Expresway before Subang Jaya exit | 19,004 | 956 | 665 | 113 | 2,174 |
|  | Lebuhraya Damasara-Puchong before Sunway Toll | 31,103 | 837 | 395 | 110 | 3,244 |
|  | Jalan Tujuan, Subang Jaya | 45,302 | 4,490 | 581 | 397 | 4,662 |
|  | Jalan Kewajipan, Subang Jaya | 18,379 | 257 | 1,213 | 353 | 6,886 |
|  | Jalan Subang (to Subang Airport) | 21,626 | 1,005 | 576 | 410 | 4,028 |
|  | Lebuhraya Damasara-Puchong near KDU | 30,011 | 866 | 491 | 75 | 3,195 |
|  | Jalan SS 2, Petaling Jaya | 20,876 | 174 | 1,725 | 98 | 1,701 |
|  | Jalan 222, Petaling Jaya | 16,083 | 876 | 174 | 137 | 3,167 |
|  | Federal Highway FR2 after Motorolla Int. | 63,419 | 1,651 | 442 | 1,984 | 15,938 |
|  | Shah Alam Expresway after Puchong Jaya | 10,748 | 369 | 302 | 37 | 1,098 |
|  | Jalan Puchong | 17,605 | 542 | 1,029 | 363 | 2,767 |
|  | Puchong-Sungai Besi Bypass Road | 28,909 | 951 | 1,248 | 205 | 3,246 |

Table 4.19 – Traffic Volume (Outbound) (Cont.)

| No. | Road | Car | Lorry (mediums) | Lorry (>3axles) | Bus | Motorcycle |
| --- | --- | --- | --- | --- | --- | --- |
|  | Jalan Templer, Petaling Jaya | 11,566 | 1,103 | 16 | 73 | 2,415 |
|  | Jalan Gasing, Petaling Jaya | 22,989 | 451 | 874 | 242 | 4,046 |
|  | Jalan Klang Lama, Kuala Lumpur | 32,285 | 761 | 2,912 | 323 | 5,039 |
|  | Federal Highway FR2 after Arch | 83882 | 2383 | 713 | 2371 | 18,482 |
|  | MRRII near Kepong | 25,604 | 2,579 | 1,020 | 254 | 6,060 |
|  | Jalan Kepong | 40717 | 2698 | 509 | 1200 | 10153 |
|  | Jalan Kuching | 73887 | 4947 | 1143 | 2175 | 19008 |
|  | Jalan Gombak | 10,495 | 915 | 166 | 384 | 3,296 |
|  | Jalan Genting Klang | 22,025 | 321 | 1,913 | 379 | 5,864 |
|  | Elevated Highway, Ampang | 15,489 | 22 | 2 | 36 | 0 |
|  | Jalan Ampang near MRRII | 22,123 | 941 | 89 | 511 | 8,912 |
|  | Jalan Cheras | 29896 | 791 | 6 | 633 | 15501 |
|  | East-West Link | 33242 | 840 | 0 | 56 | 3622 |
|  | Sungai Besi Road | 27,725 | 706 | 379 | 183 | 2,839 |
|  | KL-S’ban Highway before Toll | 34,451 | 1,154 | 673 | 843 | 38,023 |
|  | Jalan Bangsar, Kuala Lumpur | 37,075 | 2,053 | 173 | 814 | 10,227 |
|  | Jalan Syed Putra | 66367 | 1527 | 251 | 780 | 12394 |
|  | Jalan Ipoh, Kuala Lumpur | 112544 | 7003 | 148 | 3116 | 28929 |
|  | Jalan Pahang, Kuala Lumpur | 26,804 | 2,117 | 223 | 1,209 | 9,695 |
|  | Jalan Ampang near Jalan Tun Razak | 20,645 | 804 | 71 | 507 | 8,660 |
|  | Jalan Kg. Pandan, Kuala Lumpur | 19,803 | 283 | 1,058 | 280 | 4,394 |
|  | Jalan Pudu, Kuala Lumpur | 27915 | 593 | 63 | 1386 | 6986 |
|  | Jalan Loke Yew | 86112 | 4752 | 62 | 173 | 41586 |
|  | Jalan Sungai Besi | 134112 | 12703 | 632 | 1901 | 30850 |

  - Existing Rail and Feeder Bus Service

    - Existing Rail Service

The rail systems reviewed were the Star LRT, Putra LRT and KTM Bhd. The level of demand along the rail routes was ascertained by review of passenger flow at each station. A cursory treatment of the Monorail was undertaken due to its introduction in late 2003.

The level of service of the PUTRA and STAR has been very high since it began operations. Service frequency is about 8 minutes during the peak and about 10 minutes during the off peak period. The main problem appears to be lack of capacity to cope with the demand particularly during the peak periods.

KTM Komuter has had dismal performance record. Trains are scheduled at 15 minutes intervals during the peak and about 25 minutes during the off peak period. However, in actual practice, the service is unreliable and rarely punctual due to train delays and cancellations. Capacity constraints are already prevalent and there is dire need to increase the number and frequency of trains.

  - STAR LRT

The STAR LRT was opened to the public in 1998 and the analysis of the passenger demand is based on the data obtained from the Sistem Transit Aliran Ringan Sdn. Bhd. The following Table 4.20 tabulates the AM and PM peak demand for the STAR LRT stations.

## Table 4.20 : Passenger Demand during AM Peak and PM Peak Hour

(STAR LRT)

| Stations | AM | PM | Total (AM & PM) | AM & PM (%) |
| --- | --- | --- | --- | --- |
| Ampang | 1109 | 986 | 2095 | 3.64 |
| Cahaya | 558 | 496 | 1054 | 1.83 |
| Chempaka | 1418 | 1260 | 2678 | 4.65 |
| Pandan Indah | 496 | 441 | 937 | 1.63 |
| Pandan Jaya | 1160 | 1031 | 2191 | 3.81 |
| Maluri | 1131 | 1005 | 2136 | 3.71 |
| Miharja | 406 | 361 | 767 | 1.33 |
| Chan Sow Lin | 265 | 236 | 501 | 0.87 |
| Pudu | 1356 | 1205 | 2561 | 4.45 |
| Hang Tuah | 1207 | 1073 | 2280 | 3.96 |
| Plaza Rakyat | 2851 | 2534 | 5385 | 9.35 |
| Masjid Jamek | 5439 | 4835 | 10274 | 17.84 |
| Bandaraya | 2071 | 1841 | 3912 | 6.79 |
| Sultan Ismail | 571 | 507 | 1078 | 1.87 |
| P.W.T.C. | 1660 | 1475 | 3135 | 5.44 |
| Titiwangsa | 1706 | 1516 | 3222 | 5.60 |
| Sentul | 787 | 699 | 1486 | 2.58 |
| Sentul Timur | 658 | 585 | 1243 | 2.16 |
| Cheras | 609 | 541 | 1150 | 2.00 |
| Salak Selatan | 387 | 344 | 731 | 1.27 |
| Bandar Tun Razak | 972 | 864 | 1836 | 3.19 |
| Tasik Selatan | 1210 | 1076 | 2286 | 3.97 |
| Sungai Besi | 712 | 633 | 1345 | 2.34 |
| Bukit Jalil | 1125 | 1000 | 2125 | 3.69 |
| Sri Petaling | 620 | 551 | 1171 | 2.03 |
| Total | 30484 | 27095 | 57579 | 100.00 |

Source: 	Extracted Data from STAR LRT, July 2002

It was observed that Masjid Jamek station had the highest total no. of passengers travelling through during peak hours. This accounts for 17.8 % of the total passengers commuting on STAR LRT line. Masjid Jamek Station is particularly favoured by commuters due to the function of that station as a transfer station between the PUTRA and STAR lines. Furthermore, Masjid Jamek station is located within the hub of the KL Central Business District, close to employment centres. Plaza Rakyat station, with the second highest demand among STAR LRT commutors, is influenced by the location of Puduraya Bus terminal which is located within the acceptable walking distance from the LRT station. Plaza Rakyat station also caters for a combination of work, leisure and shopping trips. A number of hotel, shopping complex and cinemas are concentrated in this area.

  - PUTRA LRT

Demand for PUTRA LRT was found to be the highest at Masjid Jamek Station with approximately 13.9 % of the total of the peak person trips. Masjid Jamek caters for large passenger movement due to its function as transfer point to the STAR LRT system. The following Table 4.21 below tabulates the AM and PM peak demand for the PUTRA LRT stations.

## Table 4.21 : Passenger Demand During AM Peak and PM Peak Hour.

## (PUTRA LRT)

| Stations | AM | PM | Total (AM & PM) | AM & PM (%) |
| --- | --- | --- | --- | --- |
| Kelana Jaya | 2209 | 1964 | 4173 | 3.8 |
| Taman Bahagia | 1903 | 1692 | 3595 | 3.3 |
| Taman Paramount | 1062 | 944 | 2006 | 1.8 |
| Asia Jaya | 1761 | 1565 | 3326 | 3.1 |
| Taman Jaya | 2274 | 2021 | 4295 | 4.0 |
| University | 2236 | 1988 | 4224 | 3.9 |
| Kerinchi | 1433 | 1274 | 2707 | 2.5 |
| Abdullah Hukum | 304 | 270 | 574 | 0.5 |
| Bangsar | 2768 | 2461 | 5229 | 4.8 |
| KL Sentral | 4996 | 4441 | 9437 | 8.7 |
| Pasar Seni | 5639 | 5013 | 10652 | 9.8 |
| Masjid Jamek | 8012 | 7121 | 15133 | 13.9 |
| Dang Wangi | 1283 | 1141 | 2424 | 2.2 |
| Kg. Baru | 1114 | 990 | 2104 | 1.9 |
| KLCC | 6964 | 6190 | 13154 | 12.1 |
| Ampang Park | 3192 | 2838 | 6030 | 5.6 |
| Damai | 716 | 637 | 1353 | 1.2 |
| Dato’ Keramat | 715 | 636 | 1351 | 1.2 |
| Jelatek | 1278 | 1136 | 2414 | 2.2 |
| Setiawangsa | 1639 | 1456 | 3095 | 2.9 |
| Wangsa Maju | 2963 | 2633 | 5596 | 5.2 |
| Taman Melati | 1487 | 1321 | 2808 | 2.6 |
| Terminal Putra | 1529 | 1359 | 2888 | 2.7 |
| Total | 57477 | 51091 | 108568 | 100.0 |

# Source:	Extracted Data from PUTRA LRT, August 2002

  - KTM Bhd

The highest KTM Komuter passenger demand is at the Kuala Lumpur Station followed by Bank Negara, Kajang and Serdang stations. This high demand is attributable to job opportunities, commercial areas and a high population concentration in the area. Table 4.22 shows the morning and evening peak passenger demand.

## Table 4.22 : Passenger Demand During  AM Peak and PM Peak (KTM Bhd)

| Stations | AM | PM | Total (AM & PM) | AM & PM (%) |
| --- | --- | --- | --- | --- |
| Angkasapuri | 80 | 71 | 151 | 0.8 |
| Bangi | 122 | 108 | 230 | 1.2 |
| Bank Negara | 622 | 553 | 1175 | 6.2 |
| Batang Benar | 66 | 58 | 124 | 0.7 |
| Batu Tiga | 287 | 255 | 542 | 2.8 |
| Bandar Tasik Selatan | 317 | 281 | 598 | 3.1 |
| Bukit Badak | 20 | 17 | 37 | 0.2 |
| Jalan Kastam | 23 | 20 | 43 | 0.2 |
| Jalan Templer | 50 | 45 | 95 | 0.5 |
| Kajang | 610 | 542 | 1152 | 6.0 |
| Kepong | 373 | 331 | 704 | 3.7 |
| Kg. Dato Harun | 19 | 17 | 36 | 0.2 |
| Kg. Raja Uda | 26 | 23 | 49 | 0.3 |
| Klang | 331 | 295 | 626 | 3.3 |
| KL Sentral | 413 | 367 | 780 | 4.1 |
| Kuala Lumpur | 966 | 858 | 1824 | 9.6 |
| Kuang | 123 | 109 | 232 | 1.2 |
| Labu | 45 | 40 | 85 | 0.4 |
| Nilai | 342 | 304 | 646 | 3.4 |
| Padang Jawa | 114 | 101 | 215 | 1.1 |
| Pantai Dalam | 122 | 108 | 230 | 1.2 |
| Pelabuhan Klang | 149 | 132 | 281 | 1.5 |
| Petaling | 125 | 111 | 236 | 1.2 |
| Putra | 524 | 466 | 990 | 5.2 |
| Rawang | 450 | 400 | 850 | 4.5 |
| Salak Selatan | 63 | 56 | 119 | 0.6 |
| Segambut | 140 | 124 | 264 | 1.4 |
| Sentul | 140 | 124 | 264 | 1.4 |
| Seputih | 136 | 121 | 257 | 1.3 |
| Serdang | 592 | 526 | 1118 | 5.9 |
| Seremban | 519 | 461 | 980 | 5.1 |
| Seri Setia | 92 | 82 | 174 | 0.9 |
| Setia Jaya | 191 | 170 | 361 | 1.9 |
| Shah Alam | 524 | 466 | 990 | 5.2 |
| Subang Jaya | 494 | 439 | 933 | 4.9 |
| Sungai Buloh | 425 | 378 | 803 | 4.2 |
| Teluk Gadong | 47 | 42 | 89 | 0.5 |
| Teluk Pulai | 55 | 48 | 103 | 0.5 |
| UKM | 363 | 322 | 685 | 3.6 |
| Total | 10100 | 8971 | 19071 | 100.0 |

Source:	Extracted Data From Monthly KTM Komuter Ridership, 2002

  - Monorail

The Monorail started operations in August, 2003. There are 11 fully elevated stations located 600 - 1,000 metres apart. The KL Monorail is capable of handling up to 20,000 passengers per hour per direction, operating at up to 2 minutes headway between trains. Travelling time along the 8.6km route from Titiwangsa station to the KL Sentral station is approximately 18 minutes. The following Table 4.23 shows the Operational Characteristics of the Monorail.

## Table 4.23 : Operational Characteristics of the Monorail

| No. | Description | Parameters |
| --- | --- | --- |
| 1. | Operating hours | 7.00 am to 10.00pm |
| 2. | Maximum train speed | 80 km per hour |
| 3. | Average train speed | 30 km per hour |

The total ridership will reviewed at the end of first year of operations ie August 2004. Currently, the train operates at between 8 and 10 minutes frequency during the peak and off peak period. The main problem appears to be the lack of capacity, particularly during the peak periods. Train punctuality is good but the comfort levels are low due to excessive noise and vibration.

    - Feeder Bus Service

- Existing Conditions (Headway)

A significant component of public transport travel to other than in-vehicle time is waiting and walking/transfer times. The following Table 4.24 outlines the findings of these surveys:-

- The following feeder bus routes involve long routes which results in a very long on-board travel times;

Putra : Kelana Jaya Station : Subang Parade Route,

Putra : Dato’ Keramat Station : 916FB2 Route.

Both these routes involve journeys that exceed on one hour.

- It was found that all feeders (Putra and Star) average about 30 minutes waiting time during peak hour and involve longer waiting periods during non-peak hours. The routes with headways longer than 40 minutes are:-

## Table 4.24 : Feeder Bus Routes with Headway

## Exceeding Than 40 Minutes.

| Service | Station | Bus Route | Headway | Period |
| --- | --- | --- | --- | --- |
| Putra | Kelana Jaya | Subang Parade | 1 hour | Non-Peak |
| Putra | Asia Jaya | Taman Jaya | 2 hours | AM-Peak |
| Putra | Taman Melati | Pasar Gombak | 2 hours | AM-Peak |
| Putra | Gombak | Taman Sri Gombak | 1 hour | Non-Peak & PM Peak |
| Putra | Gombak | Sri Murni | 1 hour | AM Peak & Non Peak |
| Putra | Gombak | Greenwood | 1 hour | Non-Peak & PM-Peak |
| Putra | Gombak | UIA | 1 hour | AM Peak |
| Star | Salak South | BP11A | 1 hour | AM Peak |
| Star | Sri Petaling | Sri Petaling | 1 hour | Non-Peak, PM Peak |

Source:	BRIS Study Bus Surveys, 2002

It is very evident that these feeder routes need more buses to operate under 30 minutes headway.

- Existing Conditions (Utilisation Ratio)

The following analysis involves utilisation ratios of feeder services. The Utilisation ratio is the total no. of passengers that can be theoretically be accommodated by a bus at that station. For all intent and purposes if it exceeds 0.85, it requires the provision of additional capacity.

The stations (and feeder bus services) with utilisation ratios that exceed 0.85 are tabulated in Table 4.25.

## Table 4.25 : Feeder Services with Critical Utilisation Ratios.

| Service | Station | Bus Route | Period (Time of Day) | Utilisation Ratio |
| --- | --- | --- | --- | --- |
| PUTRA | Kelana Jaya | FAS | AM Peak/ Off Peak | 0.88/ 1.00 |
| PUTRA | Asia Jaya | Subang Parade | AM Peak/ Off Peak/ PM Peak | 0.90/ 1.00/ 0.92 |
| PUTRA | Asia Jaya | Taman Jaya | AM Peak | 1.04 |
| PUTRA | Universiti | Universiti Malaya | AM Peak/ PM Peak | 1.13/ 0.94 |
| PUTRA | Bangsar | 908B | AM Peak | 0.95 |
| PUTRA | Taman Melati | Pasar Gombak | PM Peak | 0.88 |
| PUTRA | Taman Melati | Danau Kota | PM Peak | 1.10 |
| PUTRA | Gombak | MRRII | PM Peak | 0.88 |
| PUTRA | Gombak | Greenwood | PM Peak | 0.88 |
| PUTRA | Setiawangsa | Jalan Enggang | PM Peak | 0.98 |
| STAR | Ampang | 10B | PM Peak | 1.07 |
| STAR | Cempaka | BP9C | PM Peak | 1.18 |
| STAR | Pandan Jaya | BP8A | PM Peak | 1.62 |
| STAR | Sentul | Sentul | PM Peak | 0.93 |

Source:	BRIS Study Bus Surveys, 2002

- Existing Conditions (Bus Trips)

The highest percentage of commuters use the feeder bus service to arrive at the LRT station. For the STAR service, this represents 67% of the ridership volume while it is 66% for the PUTRA service. The commutors on the LRT feeder services also originate from walking trips, bus trips and people dropped off by cars. Effectively what this highlights is that about 30% of the ridership volumes in the feeder buses do not originate from LRT trips but rather originate from walking, bus and car drop of trips. In terms of trip purpose, the major trip purpose for the feeder bus users are trips to work, followed by home based trips and school bound trips. Shopping and social trips make up only a very minimal portion of the feeder bus trips.

A large percentage of users (STAR-71%, PUTRA-81%) use the feeder bus service more than 3 times a week. The findings of the trips purpose survey indicates that the majority of the trips are; trips to work, home based trips and school bound trips. The trip purpose appears to be regular and occurs throughout the week.

About 20% of the commutors use the service either irregularly or less than 2 times in a week. This emphasises the need for effective information to be provided to the user, since about one-fifth of the users are irregular commuters.

- Existing Conditions (Service Levels)

About 75% of the PUTRA and STAR feeder bus users find the current flat fare rates to be acceptable while 20% of STAR users and 23% of PUTRA users consider it cheap. Overall only 5% of the STAR feeder bus users and 3% of the PUTRA feeder bus users consider the current fare structure to be expensive.

Table 4.26 illustrates the response of feeder bus users on the waiting time during peak and non-peak periods.

## Table 4.26 : Frequency of Feeder Buses During Peak and Non-Peak Periods.

| Frequency | Peak Hour | Non- Peak Hour |
| --- | --- | --- |
|  | STAR | PUTRA | STAR | PUTRA |
| 1 bus/15 min. | 20% | 26% | 7% | 11% |
| 1 bus/30 min. | 43% | 54% | 30% | 38% |
| 1 bus/45 min. | 25% | 12% | 33% | 29% |
| 1 bus/hr. | 12% | 8% | 30% | 21% |

Source:	BRIS Study Passenger Interview Survey by Consultant, September 2002.

The headway of the majority of feeder buses is 30 minutes during the peak hours for both STAR and PUTRA services. 37% of the public found the STAR feeder service to have headways of more than 45 minutes. About 20% of users have found PUTRA feeders to have headways of more than 45 minutes. During the off-peak periods, 63% of STAR and 51% of LRT commutors found headways exceeding 45 minutes.

The opinion survey findings gathered from feeder bus users for STAR and PUTRA is tabulated below in Table 4.27.

Table 4.27 : Opinion Survey Findings on Feeder Bus Service.

| Criteria | Star | Putra |
| --- | --- | --- |
|  | Very bad/ Bad | Average | Good/ Very Good | Very Bad/ Bad | Average | Good/ Very Good |
| Punctuality | 47% | 35% | 18% | 37% | 37% | 26% |
| Bus Condition | 43% | 37% | 21% | 18% | 39% | 43% |
| Comfort | 44% | 34% | 22% | 22% | 40% | 38% |

Source:	BRIS Study Passenger Interview Survey, September 2002

The majority of STAR feeder bus users consider the punctuality (47%), bus condition (43%) and bus comfort (44%) to be unsatisfactory. The PUTRA feeder bus service is perceived to be unsatisfactory in the following order:- punctuality (37%), Bus Condition (18%) and Comfort (22%). The overall findings indicate that the feeder bus service needs to be improved terms of punctuality, bus quality and comfort.

- Existing Conditions (Recommendations from BRIS Study)

It is very evident that most LRT stations require additional feeder buses to accommodate the travel demand. The feeder bus supply needs to be rescheduled to facilitate a frequency of at least 1 bus per 15 minutes during the peak period.  The following is a summary of the recommendations:-

- Increase the number of buses.

- Improve the condition of buses.

- Provide a frequency of 1 bus/15 min.

- Improve the punctuality of the feeder buses

# Footnotes

All information in the section on Rail and Feeder Buses was sourced from the following Report

‘A Study on an Integrated Bus Routing System in the Klang Valley’. Sections 3.0, 4.0 and 5.0.