## Slide 1: Using agent-based modelling to depict basin closure in the Naivasha basin, Kenya: a framework of analysis
P. R. van Oel, A. van der Veen, R. Becht

## Slide 2: EOIA Naivasha project
Earth Observation (EO)
Integrated Assessment (IA) Modeling
Stakeholder meetings and communication
Hydrology study
Socioeconomic study
Governance study
Limnology study
Ecology study

## Slide 3: The Naivasha basin

## Slide 5: (River) Basin closure
River basins or sub basins are closed when commitments cannot be
met (Molle et al., 2010)
Payment for Environmental Service (PES)
Environmental Service (e.g. runoff)
River basin
Hydraulic link
Local resource
Lake system
Socioeconomic link

## Slide 6: Agent-based modelling
Autonomous, interacting agents.
Many ABMs involve spatiotemporal framework.
Agents satisfy internal goals
using (nonlinear) rules, leading to decisions and actions
Agent rules may be based on:
  Rationality
  Heuristics
  Learning
Model outcome: emergent patterns at higher level of aggregation

## Slide 7: Objective of This study
Explore how ABM can be used for analyzing basin closure in
Naivasha, Kenya
Moreover, exploring the effectiveness of PES by studying emergent
patterns at the basin level

## Slide 8: METHOD
Agent behavior (alternative livelihoods: water use, land use)
  Agent strategies influenced by:
    Local resources (e.g. water, infrastructure)
    Socio-economic network (copy successful behavior, trading)
    Experiences in recent years (rainfall, experiences other agents)
Emergence at the basin level
  Spatiotemporal patterns of water availability (basin closure)
  Land cover patterns

## Slide 9: Levels of decision-making
Basin level authority
Sub basin level (user associations)
Local level (resource users)
WOTRO EOIA project Naivasha
9

## Slide 10: Model overview
State variables and scales:
Temporal extent: several decades, 1-day time-step
Water availability in local resources
Water management decisions at the basin level (e.g. lake levels)
Processes and scheduling:
biophysical dynamics (hydrology, plant growth)
land use decisions by local agents
water management decisions

## Slide 11
P
E
R
Q
P
ET
S
W
R
Inundation
zone

## Slide 12: ABM model

## Slide 13: Model test (Physical)
Meteorological data 1960 -1980
PES Scenario A: 25% farmers irrigate crops
PES Scenario B: 25 % farmers change cropland into grassland

## Slide 14: Results: Lake levels

## Slide 15: Results: Lake levels

## Slide 16: OUTCOME preliminary results
The impact of changing land use is limited with regard to runoff
The impact of water abstractions for irrigation is considerable
This suggests that PES should aim at limiting excessive irrigation
rather than restoring natural vegetation

## Slide 17: Results: Downstreamness (Dx) *
Every location x can be characterized by the size of its upstream catchment (Aup,x) relative to total basin (Atot)
x
Aup,x

## Slide 18: downstreamness of water availability (WA)
DWA changes as volumes at different locations change. For a basin with n local resources the DWA is:
Time
100%
0%
DWA

## Slide 19: downstreamness of water availability (DWA)

## Slide 20: CONCLUSIONs
The use of spatially-explicit ABM is a relevant tool for:
  Studying basin closure
  Studying the process of adoption of PES
  Analyzing the effectiveness PES at the basin level

## Slide 21: FUTURE WORK
Surveys in the field for designing valid heuristic models of decision-making by agents
The model may be extended to also indicate impacts of PES on:
  Water quality
  Socio-economic indicators
  Ecological indicators.

## Slide 22
Questions?

## Slide 23: EOIA PROJECT APPROACH 2010 - 2014
Defining the project
problem, system, indicators, scenarios
x,t scales
Database
Stakeholder process (II)
Modeling and assessment
Evaluation of results and
Visualization
Models, EO
Indicator maps (GIS)
Stakeholder process (I)

## Slide 25: FUTURE WORK
In the Naivasha basin small scale PES schemes are applied at two locations. Good opportunity for:
  validating our modeling approach
  exploring the potential
  of up scaling current PES
  schemes.

## Slide 26: DISCUSSION
For projecting the spatially-explicit developments with regard to adopting PES by individuals a process-based ABM model is preferred over a pattern-based approach (e.g. including spatial autocorrelation) because it may be
  more helpful in understanding the process of adoption
  more accurate in predicting land use change developments.

## Slide 27: EXAMPLE FOR Measuring BASIN Closure
Trend associated with minor closure
0
Change in stored volumes in upstream catchment (∆S)
Actual runoff (Q)
More natural runoff (Qnat)
Trend associated with major closure
Chart: Change in aquifer storage (106m3)
| 27205402.570897315 | 20136670.377861042 | 17255699.104468156 | 12811811.15072016 | 13388732.281963784 | 18454811.827413518 | 19390147.214134023 | 12132151.342550978 | 24524245.457720608 | 24529713.549832646 | 8629389.6121638883 | 17174355.20993004 | 23167951.515557051 | 19039798.417243086 | 12598509.57122842 | 15941342.705567731 | 18165260.107811876 | 18084279.791405376 | 20553122.868816115 | 10177170.454106744 | 8302795.2130285911
 | 71911605.0413 | 160016458.1883 | 182341115.6503 | 198556155.2448 | 186274273.747 | 105613907.5936 | 148484881.7269 | 118894104.3187 | 135279193.3328 | 105596481.2214 | 157268555.0202 | 111698922.4847 | 116656995.0659 | 102856308.5766 | 150696731.0229 | 125380194.079 | 98682487.2025 | 248726105.4849 | 186388944.3274 | 146371211.6138 | 145087049.3269
Not closed.