## Slide 1: RiskCity Introduction to Frequency Analysis of hazardous events

## Slide 2
Extreme Events
“Man can believe the impossible. But man can never believe the improbable.”
- Oscar Wilde
Linda O. Mearns NCAR/ICTP
“It seems that the rivers know the [extreme value] theory. It only remains to convince the engineers of the validity of this analysis.”
–E. J. Gumbel

## Slide 3: Objective of FA exercise
The objective of this exercise is to practice different methods of frequency analysis for floods and for earthquakes and to gain insight in magnitude – frequency relationship.
Keep in mind that the methods presented in this exercise are just a selection of all existing methods.
In this exercise ILWIS is not being used.

## Slide 4: M-F relationship
ISL 2004
Magnitude-frequency relationship is a relationship where events with a smaller magnitude happen more often than events with large magnitudes.
Magnitude is related to the amount of energy released during the hazardous event, or refers to the size of the hazard.
Frequency is the (temporal) probability that a hazardous event with a given magnitude occurs in a certain area in a given period of time.
Notes: Introduction to GIS
4

## Slide 5: M-F relationship
ISL 2004
The M – F relationship does hold true for many different disaster types, but as can be seen in the table, not for all:
 | Disaster type | Occurrence possible | M - F relationship
Hydro-meteorological | Lightning Hailstorm Tornado Intense rainstorm Flood Cyclone/ Hurricane Snow avalanche Drought | Seasonal (part of the year) Seasonal (storm period) Seasonal (“tornado season”) Seasonal (rainfall period) Seasonal (rainfall period) Seasonal (cyclone season) Seasonal (winter) Seasonal (dry period) | Random Poisson , gamma Negative binomial Poisson, Gumbel gamma, log-normal, Gumbel Irregular Poisson, gamma Binomial , gamma
Environmental | Forest fire Crop disease Desertification Technological | Seasonal (dry period) Seasonal (growing season) Progressive Continuous | Random Irregular Progressive Irregular
Geological | Earthquake Landslide Tsunami Subsidence Volcanic eruption Coastal erosion | Continuous Seasonal (rainfall period) Continuous Continuous Intermittent (magma chamber) Seasonal (storm period) | Log-normal Poisson Random Sudden or progressive Irregular Exponential , gamma
Notes: Introduction to GIS
5

## Slide 6: Flooding
Return period/exceeding probability
Extreme value distribution by Gumbel method
Intensity-duration-frequency relationships

## Slide 7
What is the return period of a rain event over a 100 mm/day ?
Maximum daily preciptation (mm)
Between 1935 and 1978: 9 events
4
1
1
16
3
6
5
5
8 Intervals, ranging from 1 to 16 years
The sum of the intervals =
4 + 1 + 1 + 16 +3 + 6 + 5 + 5 = 41
Average = 41/8 = 5.1 years
Annual exceedence probability of a rain event over 100 mm/day = 100 / 5.1 = 19.5 %
Flooding
Return period/exceeding probability

## Slide 8: Flooding
Q100 has a greater probability of occurring during the next 100 yrs (63%) than during the next 5 years ( 5%)
For the average annual risk!
Return period/exceeding probability

## Slide 9
Flooding
Frequency Analysis

## Slide 10
Flooding
0
2
4
6
10
8
12
500
550
600
650
700
750
800
850
900
450
950
Rainfall classes (mm)
Frequency
Frequency Analysis

## Slide 11
-2
+2
+3
+1
-1
-3
X
0.683
0.954
0.997
P(R < 642) = 0.5
P(R > 642) = 0.5
P(532 < R < 752) = 0.683
Mean: 642 mm
Standard deviation: 110 mm
P(422 < R < 862) = 0.954
P(312 < R < 972) = 0.997
Flooding
Frequency Analysis

## Slide 12: Flooding
Unfortunately, a large amount of events is right skewed;
Magnitude of events are absolutely limited at the lower end and not at the upper end. The infrequent events of high magnitude cause the characteristic right-skew
The closer the mean to the absolute lower limit, the more skewed the distribution become
The longer the period of record, the greater the probability of infrequent events of high magnitude, the greater the skewness

## Slide 13: Flooding
0
2
4
6
10
8
12
500
550
600
650
700
750
800
850
900
450
950
Rainfall classes (mm)
Frequency
The shorter the time interval of recording, the greater the probability of recording infrequent events of high magnitude, the greater the skewness
Other physical principles tend to produce skewed frequency distributions: e.g. drainage basin size versus size of high intensity thunderstorms.

## Slide 14: Flooding
Solution to right-skewness:
Use Extreme Value transform (other names: Double exponential transform or Gumbel transformation):
Rank the values from the smallest to the largest value
Calculate the cumulative probabilities: P=R/(N+1)*100%
Plot the values against the cumulative probability on probability paper and draw a straight line (best fit) through the points
From the line, estimate the standard deviation and mean
Estimate all other required probabilities versus values

## Slide 15: Flooding
Extreme value distribution by Gumbel method

## Slide 16: Flooding
Intensity-duration-frequency relationships
IDF curves are calculated for a certain station and it cannot be extrapolated to other areas.
Intensity
Duration

## Slide 17: Earthquakes
Per day
0.5
4
36
360 (every 4 minutes….)
3600 (every 24 seconds….)

## Slide 18: Earthquakes

## Slide 19: Earthquakes
The Gutenberg-Richter Relation
log N(M) = a – bM
Gutenberg-Richter plots are made for various data sets all over the world, and most of them end up having a b value very close to 1, usually slightly less.